## Slide 1: S-L1Calo upstream links
architecture -- interfaces -- technology

## Slide 2: what we got : current L1Calo
L1Calo real-time data path spanning 3 types of processor modules:
  pre-processor (mixed signal) operating on a granularity of .1[].1[]  (e,h)
  digital processors : CP and JEP consisting of processor modules and merger modules delivering results to CTP.
  ‘Phi quadrant architecture’
Algorithms:
  bunch crossing identification, data conditioning (gain, threshold) and compression (“BCmux”) on the pre-processors
  feature extraction: global variables and localized objects
    sliding window algorithm requires a lateral environment of .6 in  and  for jets (6 channels) .3 in  and  for , (3 channels)
    upstream link replication (38%), backplane fanout (75%)
  feature reduction : Count objects passing energy thresholds
  pass results to CTP for feature correlation

## Slide 3: what’s different / similar on S-L1Calo ?
Algorithms not yet defined in detail, but assume baseline :
let’s have just more of the same : sliding window algorithm, but expect incoming optical links carrying data at finer granularity (.05 .05), and have more information available describing longitudinal shower profile (FE feature extraction).
Some questions / issues :
route data such that they can be summed into trigger towers
think about bunch crossing identification / pre-processing
jet size, and therefore sliding window algorithm lateral environment requirements won’t change : ~ .6 in  and   fraction of duplicated channels will go up
upstream replication (optical)
downstream replication (electrical)
source
e/o
source
e/o
source
e/o
sink
o/e
sink
o/e
e/o
e/o

## Slide 4: what input do we need from frontend processors ?
Let’s assume we have ‘intelligent’ programmable data sources.  Have them
care about bunch crossing identification
  per cell ?
  per trigger tower ?
pre-sum and condition the data such that we can
  optimize granularity (performance vs. environment)
  optimize upstream link replication - ideally the copies are not exact copies of another link, but rather separately built streams (requires duplication of serializer in addition to duplication of e/o converter)
possibly have some “BCmux” style data compression on the links ?
transmit the data at convenient rates and formats over ‘standard’ opto links : today’s (affordable) technology is limited to 6 Gb/s per lane, but...

## Slide 5: technologies : serdes and o/e converters
The need for high bandwidth data transmission, in particular for network processor applications, has brought us new and improved standards on paper and on silicon.
link speeds on existent high volume products scaling up now (SAS2.0/SATA3.0 @ 6 Gb/s electrical)
network processor protocols (Interlaken / SPAUI / SPI-S) build on scalable high speed link definitions OIF-CEI-6G, -11G, -25G
100 GbE using up to 25 Gb/s lanes
FPGA on-chip links currently support up to 48 CEI-6G lanes (ie. aggregate bandwidth of 36 Gigabyte/s per FPGA)
parallel opto links (SNAP12/MSA) are available up to 10Gb/s per lane
low power (~1W) mid-board mount SNAP12 devices (fibre pig-tail) move O/E converters away from board edge so as to improve density, routability and signal integrity
AdvancedTCA allows to route 10Gb/s lanes on a backplane
 6Gb/s is certainly doable now , but we might be able to benefit from evolution if we avoid freezing the concept too soon...

## Slide 6: example : re-do current L1Calo at finer granularity (23)
Sliding window processor, same concept, same partitioning...
assume unchanged pre-processing, but upstream optical links at .05.05 granularity, ie. 16384 towers, 20 bit per tower (LAr+tile), 40 MHz bunch clock
4 processor crates, each processing one quadrant in phi, 8 modules per crate (ATCA)  512 towers per module
37.5% upstream link replication (phi)  1.375  512  20  .04 Gb/s = 564 Gb/s per module  8 SNAP12 devices per module at 5.9 Gb/s per lane
feasible, but already challenging due to board area (need some space for FPGAs !) and level of electrical link replication on the backplane
for higher data volume go to phi octant scheme, increasing upstream link replication. 16-slot ATCA is unfortunately 23” wide...
Higher per-link bandwidth would help !

## Slide 7: Conclusion
we cannot spread L1Calo over large number of crates, need a high density processor, due to environment processing
need to use opto devices and serdes with minimum footprint per Gigabit. Watch the markets...
need to offload some pre-processing to the calorimeter ROD / FE modules to allow for compact processing on L1Calo
be aware of possible issues routing the data where they are needed (patch panels)