## Slide 1: Mainz R&D activities

## Slide 2: MZ R&D
BLT has been built and tested (backplane transmission only). A few minor issues were found.
Possible future firmware / test activities on the BLT:
  TTC clock / data recovery
  Multi-Gb/s links (opto inputs / outputs)
  SystemACE configuration scheme
Hardware activities
  build another copy of the BLT, if required. Minor h/w fixes. Might act as CMM demonstrator. Dead end due to Virtex-5 chip.
  build a Generic Opto Link Demonstrator (GOLD) ATCA module
    Optical data replication on fibre (splitter/coupler)
    Optical feed-through from backplane
    O/E conversion and replication (CML fan-out) on module
    Array of moderately sized FPGAs (Virtex-6)
    Module control via serialized VME-- (optical)
    Bruno has started work...

## Slide 3: CMM++

## Slide 4: Some Remarks on CMM++
CMM++, as presented here, is an excellent scheme to combine a high performance, high link speed phase-1 backplane data extractor with a legacy daisy-chained merger. A demonstrator does actually exist already: BLT - electrical in, optical in/out.
CMM++ concept seems to aim at full plug-in compatibility with the current system. However, the RTDP is just a fraction of a module. There are less exciting parts : VME / CAN / TTC /... For full s/w and maximum f/w compatibility these will probably have to be built along the current CMM scheme. Mainz style all-in-one-FPGA won’t be possible without major f/w and s/w effort.
Do we (who ?) want to spend that extra effort on plug-in compatibility ? What level of differences to current modules do we accept ?
Since we are probably talking production modules , the functionality required ( including backwards compatibility) will have to be discussed in a proper review procedure.

## Slide 5: Alternative roadmap
Slightly different roadmap in case we do not spend effort on compatibility mode
Do a demonstrator for global processor asap
  Could well be Mainz GOLD demonstrator based
  Include a compatibility mode that allows to bypass the processor and route the current L1Calo CTP signals through to the CTP (switchable per processor : cluster, jet, energy)
  Request some space close to CTP already now !
For the time being, exercise the global processor with BLT based modules
Build proper CMMs, based on Virtex-6 later (similar to the ones suggested today)
Gradually change over from current L1Calo to phase1 processing by replacing CMMs and switching mode for the respective channels on the global processor