## Slide 1: (Not just) Backplane transmission options

## Slide 2: So far
Preliminary design for phase 1 had been suggested
  Extract topological information from digital processors (firmware upgrade)
  Replace CMMs by serialiser w. fibre output
    Up to 160 Mb/s backplane data rate
    3 Gb/s optical out
  Aggregate bandwidth at merger slot 64 Gb/s
  Total bandwidth of JEP and CP ~700 Gb/s
  Two-stage top level calorimeter processor (quadrant)
Hard facts on backplane bandwidth limits
Detailed algorithms
Simulation
Muons

## Slide 3: Recently...
Some backplane results:
  160 Mb/s possible
    Need separate clock line ?
  ... even with CMM (Richard, CPM only)
  Higher rates possible only with sink termination
Some simulation results
(non-)schedule seems to be sliding
Technology moves on
BTW: are we really sure the current trigger scheme is good enough for design luminosity (phase 0) ?
 Difficult to judge as long as there are no collisions at all !

## Slide 4: What can we do by firmware only ? – backplane
We can be rather sure that 80 Mb/s backplane operation suits current CMMs
120 Mb/s would probably require clean external clock, due to Virtex-E DLL limitations :
  Spare differential inputs in the back of a CMM
  SFP o/e transceiver cheap and low jitter
Signal integrity seems ok even for 160 Mb/s
At an elevated data rate the data windows shrink due to known jitter and walk from TTCdec (TTCrx).
 Need a per-slot phase optimization at source
  JEP: clkdes1/2 are in use. Could be made available (major f/w mod on input processor), s/w
  CP:

## Slide 5: And on to the CTP
Probably quite some spare bandwidth on the CMM outputs
  To run at 80 Mb/s ?
LVDS signalling rate depends on cable length and cable properties, double rate should be ok.
Conversion to optical rather simple if DC balanced (firmware, SNAP12/MPO : $)
  Will require conversion to electrical at CTP end?
Need detailed assessment of CMM capabilities
Nothing known about CTP inputs (?)

## Slide 6: Algorithms : just an example...
Most algorithms of which we expect performance gains require massive increase in data rate throughout the system  not for phase 0
  Let’s use most simple ones?
  Keep existing data from CMM to CTP?
Leading jets angle cuts require two most energetic ROIs only:
  Moderate bandwidth requirement
  Sort algorithm required at all stages
    JEM: 2 of 8
      RoI position and threshold? Data format and b/w?
    Crate merger : 2 of 32
    System merger: 2 of 4
  Calculation of angle and thresholding (LUT)

## Slide 7: Phase 1
Backplane
  CP rates probably limited to 160 Mb/s
    Data format?
  JEP possibly higher if required (termination)
Merger links (optical)
  Xilinx Virtex-5/6 stuck at 6.5 Gb/s (2010/11)
  Aggregate bandwidth ~200 Gb/s per chip
  No information on Virtex-6 HXT (10 Gb/s)
Merger could be ATCA or similar form factor
    But LaCalo VME legasy?
Optical components for high density processors available
  High density blind mate opto backplane connectors
  Splitters
  MPO fanout
  (Optical backplanes too exotic)

## Slide 8: Plans
Improve performance of current system (firmware)
Devise and simulate algorithms for phase 1
Make optimum use of existent demonstrators
  Stockholm link tester generate 3.2 Gb/s optical
  BLT serialise backplane data to 6.5 Gb/s optical
Build a demonstrator global merger with 6.5 Gb/s links
  “Inverse” use of BLT as receiver?
Design for unrestricted choice of algorithms:
  restricted only by the CP/JEm backplane bw
aim to feed maximum of data into single point  maximum link density, high performance FPGAs
  “single box” approach?
Discuss timeline  decide on
  Form factor
  Amount of processing power required
  Signal replication scheme
    Extensive use of optical technology
    Replication at source
    Electrical multi-Gb/s link replication at sink

## Slide 9: To Do – Who – What ?
Mainz interested in
  Firmware-based improvements on current JEMs
  6.5 Gb/s FPGA based link technology
  Optical : passive replication – blind mate connector
  Ready to work on global merger demonstrator
  Not yet given up on possible JEM rebuild
MSU: interested to join the GM demonstrator activity
  output from “VHDL framework”
  data formats, algorithm implementation