## Slide 1: Ethernet-driven control and data acquisition scheme for the Timepix-based TPC readout
R. Degele, C. Kahra, U. Schäfer, M.Zamrowski
Univ. Mainz

## Slide 2: TPC readout chain
TPC to be read out by one or several pixel sensors (256*256 pixels)
Timepix chip bonded on a FR4 carrier
  Amplifier
  Discriminator
  TDC
    TOT
    Common stop
  Serialiser (LVDS link)
Flat cable connection (ZIF) to adapter board
  Trigger, test pulse, voltage monitor
Flat cable connection to Xilinx ML506 evaluation board
  FPGA Virtex-5 (XC5VSX50-TFFG1136)
    Deserialiser
    Buffer
    Ethernet / IP packet engine (UDP)

## Slide 3: TPC readout chain
TIMEPIX-
ADAPTER-
BOARD
ML506
ETHERNET
Timepix chip
GEM
Ionizing particles
cathode

## Slide 4: Adapter board
          Testpulse generator
ADC
4-Channel
24-Bit
Voltage
Reference
2V5
Connector to Xilinx ML506
Trigger
RJ45
(TLU)
ID -NUMBER
TRIGGER, BUSY, RESET, DATA CLOCK
control
DAC-OUT
TEST_IN
3V
3V, 5V
5V
S/N
2V2
7V
CONTROL, CLK, ADDRESS
Connector to Timepix
Power supply
DAC-OUT DIGITAL
TIMEPIX-CONTROL
TIMEPIX-DATA (LVDS)
TP_IN

## Slide 5: Timepix