## Slide 1: Ethernet-driven control and data acquisition scheme for the Timepix-based TPC readout
R.Degele, C.Kahra, U.Schäfer, S.Tapprogge, D.Wicke, M.Zamrowski
Univ. Mainz

## Slide 2: TPC readout chain
TPC to be read out by one or several pixel sensors (256*256 pixels)
Timepix chip bonded on a FR4 carrier
  Amplifier
  Discriminator
  TDC
    Time Over Threshold
    Common stop
  Serialiser (LVDS link)
Flat cable connection (ZIF) to adapter board
  Trigger, test pulse, voltage monitor
Flat cable connection to Xilinx ML506 evaluation board
  FPGA Virtex-5 (XC5VSX50-TFFG1136)
    Deserialiser
    Buffer
    Ethernet / IP packet engine (UDP)
Ethernet link to computer

## Slide 3: TPC readout chain
TIMEPIX-
ADAPTER-
BOARD
ML506
ETHERNET
Timepix chip
GEM
Ionizing particles
cathode

## Slide 4: Lab test setup
Programmer
Flat cable
Xilinx ML506
Adapter
Flat cable
Timepix
Ethernet to computer

## Slide 5: Timepix
256*256 channel matrix
55µm * 55µm pitch
Analogue input stage with per-pixel threshold adjust
Digital TDC w. 14-bit LFSR counters @ up to 100MHz
Several conversion modes incl. TOT and common stop
  shutter input
No zero suppression
Serialisation of matrix data (~1Mbit) into LVDS output
Auxiliary controls:
  Test pulse in
  Diagnostics : analogue monitor for internal current sources (DAC_OUT)

## Slide 6: Timepix
55µm
20µm
10µm
Pixel cell

## Slide 7: Timepix – a few particularities
There exists a global threshold setting (THL, 14-bit)
Pixels can be threshold-corrected individually by a 4-bit value.
Range of threshold correction is set globally (THS)
Above global settings and other current source settings can be read back as analogue voltages via DAC_OUT pin for diagnostic purposes
Counters are 14-bit Linear Feedback Shift Registers = Pseudo Random Number Generators
  Require linearisation so as to recover the time/amplitude information
  Require special consideration if zero suppression or thresholding are to be done
Serial communication done by a simple clock/data/enable interface, through shift register

## Slide 8: Adapter board
          Testpulse generator
ADC
4-Channel
24-Bit
Voltage
Reference
2V5
Connector to Xilinx ML506
Trigger
RJ45
(TLU)
ID -NUMBER
TRIGGER, BUSY, RESET, DATA CLOCK
control
DAC-OUT
TEST_IN
3V
3V, 5V
5V
S/N
2V2
7V
CONTROL, CLK, ADDRESS
Power supply
DAC-OUT DIGITAL
TIMEPIX-CONTROL
TIMEPIX-DATA (LVDS)
TP_IN
Connector to Timepix

## Slide 9: Adapter board
Trigger
To ML506
To ML506
To Timepix
Power
Test pulse in

## Slide 10: FPGA module : Xilinx ML506
  Virtex-5 based : XC5VSX50-TFFG1136
  On-chip Ethernet MAC
  On-chip 3Gb/s serial links : run at 1Gb/s for Ethernet
  On-board Gigabit Ethernet phy chip (1000BASE-T)
  64 bit user I/O on 2.54mm headers
  Nonvolatile configuration storage via SystemACE (CompactFlash card)
A lot of periphery, not currently used for Timepix readout

## Slide 11: FPGA Firmware
VHDL description
Common clock for digitisation and data transfer, crystal based, frequency currently hard coded in VHDL
SerDes interface to the Timepix bit-serial port
Control and status registers, data stream pass-through
Network communication based on Xilinx-supplied Ethernet macro (TEMAC wrapper)
  No embedded CPU
  Minimalist network protocol stack
    UDP only
    No management protocols (ARP etc.)
Shutter operated under software control or in response to a trigger (TLU) with programmable delay and width
Timepix protocol not fully understood from documents  modelled on MUROS2 readout scheme

## Slide 12: Firmware : Data transport to computer
Data transmission scheme to readout PC using UDP protocol:
<ethernet><IP><UDP><control><data>
standard Ethernet/IP/UDP headers
18-byte control field mapped to register file within the FPGA (control and status words)
Variable length data field carrying data to/from Timepix chip
Timepix matrix data not buffered on FPGA, data kept on Timepix while awaiting packet transmission
Data pulled by computer (handshake)

## Slide 13: Control software
C++
Currently command line interface only, no GUI
Base functionality:
  Reset Timepix
  Set current sources (write FSR)
  Enable test pulse
  Set Timepix matrix
  Read out matrix
  Operate shutter
Complex operations
  Start a run : initialise matrix and read it out upon reception of a trigger, linearise data, write to file
  Pixel calibration

## Slide 14: Pixel calibration
Intercalibrate all pixels so as to achieve a uniform noise level across the whole of the chip
Measure noise in TOT mode for a fixed period of time
Repeat the measurement for
  All global threshold settings ( 0 to 16383) (THL)
  All per-pixel threshold corrections (0 to 15)
  A pre-set correction scale (THS, 0 to 255)
Calculate optimum per-pixel correction values
Software status:
Base functionality and run control done
Pixel calibration s/w development under way
To do: read back current source data (DAC_OUT)

## Slide 15: Tests / Results
Timepix and readout wired up in the lab (Mainz)
Run with TPC in Bonn
Readout working at
  Event rates up to 23 Hz @ 40MHz system clock ++
  Scaling to 33 Hz @ 100MHz clock
  Readout rate of bare Timepix would be (100Mbit/s) / 1Mbit = 100Hz
  FPGA code pipelined, packet overhead is low
  FPGA currently polled by PC, i.e. handshake for each packet transmitted
   Bottleneck probably due to latency in Linux IP stack

## Slide 16: Results: Some basic sanity checks ...
Noise @ threshold THL=290, common stop mode
8000 test pulses, counter mode. 17*13 pixel clusters masked out

Locally induced noise, “written” to Timepix sur-face with a pulser and an insulated wire 
Timepix pixel matrix 256*256

## Slide 17: Results: muons in the TPC
Energy deposit  (TOT mode)
X-Y-Zdrift view 
(common stop mode)
Muon tracks crossing the TPC  at 8.9cm and 2.8cm  distance to readout plane.
Both deposited charge and drift time measured concurrently by operating every other pixel in TOT or common stop mode

## Slide 18: Summary / Outlook
A readout system for a TPC, with Timepix-based digitisation, has been implemented on a Xilinx ML506 development board (Virtex-5)
Data path off the FPGA into the computer via Gbit Ethernet and UDP protocol
Readout rate currently up to 33 events per second
System successfully operated in the electronics lab and on a TPC
Plans:
  Re-target to Virtex-6
  Increase event rate
  Increase channel count
  Consider zero-suppression on the FPGA
  …