## Slide 1: Multi-Gigabit transmission BLT  GOLD

## Slide 2: GOLD real-time data path and control
GOLD will be operated in conjunction with the BLT, acting as a data source and control module
GOLD residing in ATCA crate
Currently no crate CPU (nor crate...) available
Optical link to BLT (SFP) allows for module control
Optical receivers (12-channel) on RTDP
BLT residing in CMM slot of JEP crate
Controlled by VME--
Optical control link extends VME functionality to GOLD
Optical transmitter (SNAP12, up to 6.5 Gb/s) to be used as a data source
GOLD is Virtex-6 based / BLT is Virtex-5 based

## Slide 3: Module status
1 BLT available
  1 SFP link, tested up to 6.4Gb/s, ok
  1 SNAP12 link , requires minor h/w mods
  2 SNAP12 opto module pairs ordered in February, not yet arrived
  Internal clock suitable for multiples of 160 MHz
GOLD not expected in very near future
 use Xilinx development board as a GOLD emulator
1 ML605 available
  1 SFP link
  Daughter module might carry additional link hardware
  Internal clock suitable for multiples of 100 or 125 MHz

## Slide 4: Transceiver modes
Control path will probably be asynchronous eventually
  Requires buffering the received data where crossing clock domains
  Control stream will contain fill characters (comma) which can be taken out or added by clock correction circuitry so as to cope with slightly differing rates at source and sink
RTDP will probably benefit from synchronous transmission
  Requires cleaned global clock (LHC bunch clock)
  Received data are coming in at correct rate, but unknown phase offset
  Requires phase alignment
    Xilinx recipe to align phase to recovered clock (within receiver)
      Leads to separate clock domains for each data channel
      Requires yet another phase alignment to global clock in the fabric
    Try to align to one global clock per FPGA right away