## Slide 1: GOLD

## Slide 2: GOLD design
Main board:
ATCA form factor
Four input processors XC6VLXT
  Fed from mezzanine module
  144 electrical inputs total, 6.5 Gb/s each
  36 electrical outputs, 6.5 Gb/s each, for test purposes only
Low latency parallel on-board links at 1Gb/s
One main processor, 12-fibre optical output through front panel
Further connectivity (up to 10Gb/s) and processing resources via four XC6VHXT devices
DAQ/ROI
FPGA configuration (System ACE), monitoring, module control
Opto mezzanine module:
Fed from five optical backplane connectors, up to 72 fibres each
Up to twelve 12-channel optical receivers or transmitters will physically fit
Clock/control mezzanine module
Reception and conditioning of (LHC) clocks
Some general control
JTAG mezzanine module
USB connectivity for FPGA configuration/control
Pre-configuration access

## Slide 3: GOLD status
Main board
  First version ready except last minute bug fixes
  consistency checks on schematics and symbols almost finished (Eduard)
  Schematics and layout kept in sync, therefore expect readiness for production shortly after last fixes
Input module and clock module under way
Schematics for JTAG module near final
Try to have an L1Calo internal review of GOLD specifications in January
  Busy preparing documentation
  Will soon be posted at www.staff.uni-mainz.de/uschaefe/browsable/L1Calo/GOLD/GoldReview.htm
  Need a few volunteers for the review panel
Eduard started work on GOLD module services firmware
Weina started work on Algorithms
  Participate in definition of interfaces / data formats
  Low level C/++ simulation
  VHDL simulation
  Implementation in GOLD
    Jet dphi & Emiss algorithms (Carsten’s algorithms)
    Muon isolation (+ Sebastian)