## Slide 1: Level-1 Topology Processor for Phase 0/1 - Hardware Studies and Plans -
Uli Schäfer
Johannes Gutenberg-Universität Mainz

## Slide 2: Topology Processor
Simulations suggest a need for topological trigger criteria, so as to keep Level-1 trigger effective at high luminosities.
Example algorithms:
Angular correlations (jets, direction of missing energy)
Muon isolation
…
Hardware implementation
 Need to feed a maximum of data into a single point (module, FPGA)
Input from L1Calo and Muons
  ~ 1 Tb/s aggregate bandwidth
  Do not partition into multiple modules for reason of LA***CY  !
TOPO

## Slide 3: Current L1Calo Scheme
PPr
CP
JEP
CTP
Mixed Signal Pre-Processor
FPGA based digital “sliding window” processors (e/m cluster, jet/energy)
Object count and global quantities via chained mergers CMM into CTP
Object positions to Level-2 and DAQ only
analog
480Mb/s
40Mb/s
real-time paths shown only

## Slide 4: Phase 0/1 Scheme
PPr (nMCM)
CP
JEP
CTP
New CMX (CMM++) module with two interconnect options
  Chained (legacy and opto links)
  Star topology with all opto links into topology processor
Muon information included on topo processor
analog
480Mb/s
real-time paths shown only
TOPO
Muon
6.4/10Gbps

## Slide 5: … Topology Processor
Input from L1Calo and Muons
  ~ 1 Tb/s aggregate bandwidth
  Fibre optical inputs @ 6.4/10 Gbps per fibre
Output to CTP
  electrical (LVDS)
  fibre optical ~ 1Gb/s +
Interfaces to TTC/GBT/…, Level-2, DAQ, control, DCS,…
Small number of modules (~1)
Probably dedicated crate, near CTP
Have started development programme
2010 : 6.4Gb/s data source BLT in CP/JEP crates  to live in CMM slots  CMX
2011 : Topo processor demonstrator GOLD !

## Slide 6: The demonstrator : GOLD
Functional demonstrator for phase-0 topology processor
Technology demonstrator for technologies to be used throughout L1Calo upgrade programme, studies on fibre optical connectivity schemes
----->
ATCA form factor
Modular concept
  Mezzanines
  FMC connectors
Optical backplane connectors rather than front panel I/O
Opto/electrical conversion on input mezzanine
Electrical connectivity up to 10Gb/s in ATCA zone 2
Phase-0 topo-specific connectivity
  Provide all interfaces

## Slide 7: GOLD floor plan
A
C
B
D
E
F
G
H
J
Z1
Z2
Z3
V
W
X
Y
front panel connectors
Mezzanines
A-J FPGAs
Z3: opto connectors
Z2: electrical connectors
V – Y : FMC connectors
AdvancedTCA 322x280 mm

## Slide 8: GOLD - some details
Main board, ATCA sized, 22 PCB layers
FPGAs (Virtex-6 LXT, HXT)
Connectors, sockets for e/o converters
FPGA configurator and local clocks (DAQ/ROI, Ethernet,…)
Main power distribution network (central and POL regulators)
Input mezzanine module, allow for choice of input devices and input signal routing
12 layers, moderate real estate
Sockets for o/e converters, 10Gb/s fanout
Clock mezzanine module
Recover and condition incoming (LHC bunch) clocks
Some limited clock multiplexing and fan-out
Provide additional space for auxiliary components and front panel connectivity

## Slide 9: GOLD floor plan
Z1
Z2
Z3
Opto
L
L
L
L
H
H
H
H
5 * XC6VLX (Processor L, main processor M) up to 36 links each
Two pairs of XC6VHX (H) 72 links each
5+ 12-channel optos on daughter
Clock generation
144 multigigabit input links in zone 2 (equiv. 22300 bit / BC)
M
890Gb/s
total

## Slide 10: Densely packed, thick module

## Slide 11: Production and test programme
L1Calo internal review 
Some cleanup & checks on the design (couple of weeks)
PCB production, assembly ~ 2 months
On-going development of service firmware, algorithmic firmware, online software
From July 2011 available for studies on
Signal integrity and data transmission bit error rates
Latency issues
Optical interconnect schemes and link replication
 Use for
Test bench for topology algorithms
System level tests along with current L1Calo modules and CMX merger module prototypes

## Slide 12: Plans for Phase 0 / 1
Start with detailed design work on topology processor prototypes in 2011, pending
  Review availability and suitability of FPGA devices : Virtex 7 vs. Virtex 6 HXT
  Finalise optical interconnect scheme
  Review input connectivity requirements (including Muons)
  Review processing power requirements (algorithm dependent)
Commission production modules in 2013/14 shutdown
Connect up with CMX and CTP
Connect up with muons as soon as muon input signals become available
For phase 1 no hardware modifications are currently planned, unless requirements change beyond the ones known by end 2011
However, open for further improvements in next following long shutdown:
 will continue to explore upcoming technologies (opto links, FPGAs, …) and ready to leverage for possible phase1 project