## Slide 1: Phase-1 with new JEP
Uli Schäfer
Johannes Gutenberg-Universität Mainz

## Slide 2: New Jet/Energy processor
JEP will be of very old age by time of phase-1 upgrade
  Limited availability of spares
  FPGAs not supported by current design tools
LArg signals will be available optically at high granularity for phase 1
Tile optical signals might become available at a later stage
JEP comprised of JEMs, based on modular concept (mezzanines)
Staged upgrade of JEP, so as to guarantee smooth changeover.
Minimal approach:
Increase JEM optical output capacity by renewal of low-cost daughter modules
Add nJEP processor next to topology processor module, to receive JEM optical real-time output
Keep JEP running while nJEP being commissioned…
Eventually switch to nJEP based jet trigger
Use old JEMs for e/o conversion of tile signals only
Replace JEMs with simple and cheap converter modules as further spares are required
In case we were running into a latency crisis, full JEP replacement by o/e converter modules would be effective and affordable

## Slide 3: Phase-1 upgrade with new JEP
nJEP
tile
Jul. 28, nJEP
See next slide

## Slide 4: nJEP : improving performance
Minimal approach is basically just a replacement of aging JEP
nJEP to provide plenty of spare input capacity. Use it for considerable improvement of physics performance
  Improve algorithms by making use of finer granularity available from DPP
  Consider feeding nJEP directly from PPr, at granularity of up to 0.1×0.1 in η×φ
  Switch to high granularity optical input directly from tile, as it becomes available
nJEP to be built phase-2 compliant !