## Slide 1: Phase-1 with new JEP
Uli Schäfer
Johannes Gutenberg-Universität Mainz

## Slide 2: New Jet/Energy processor
JEP will be of very old age by time of phase-1 upgrade
  Limited availability of spares
  FPGAs not supported by current design tools
LArg signals will be available optically at high granularity
Tile optical signals might become available at a later stage
JEP comprised of JEMs, based on modular concept (mezzanines)
Staged upgrade of JEP, so as to guarantee smooth changeover. Minimal approach:
Increase JEM optical output capacity by renewal of low-cost daughter modules
Add nJEP processor next to topology processor module, to receive JEM optical real-time output
Keep JEP running while nJEP being commissioned…
Eventually switch to nJEP based jet trigger
Use old JEMs for e/o conversion of tile signals only
Replace JEMs with simple and cheap converter modules as further spares are required
Consider feeding nJEP directly from PPr
In case we were running into a latency crisis, full JEP replacement by o/e converter modules would be effective and affordable

## Slide 3: Phase-1 upgrade with new JEP
nJEP
tile
Jul 27, nJEP

## Slide 4: nJEP : towards phase-2
Minimal approach is basically replacement of aging JEP
nJEP to provide plenty of spare input capacity
  Improve algorithms by making use of granularity available from DPP
  Add higher granularity optical input from tile as it becomes available
nJEP to be built phase-2 compliant