## Slide 1: L1Topo-phase0

## Slide 2: Topo
GOLD successfully used to explore technologies and initially verify 6.4Gb/s link integrity over moderate length electrical traces
Complex PCB, first “ATCA” module built in MZ (not compliant)
Build prototypes now, meant to be very close to production modules
  ATCA (incl. IPMI, standard clock fabric, base interface ?)
  Two large processor FPGAs (XC7V485T)
  Some FPGA based control circuitry
  High-density opto/electrical converters (miniPOD) on main board
  No on-board electrical duplication of real-time signals
    Require upstream duplication
    Use parallel interconnect as required (latency!)
Production modules in 2013
  Larger FPGAs
  Final decision on module control: processor (ARM) vs. FPGA
  Otherwise bug fixes only

## Slide 3: Topo prototype / production
2 × XC7V485T  XC7V690T (A,B)
1 × XC7K325T (C) for all non-realtime circuitry
14 miniPOD receivers
Up to 80 links per FPGA (GTH…)
Probably up to ~11 Gb/s
Some miniPOD transmitters (including DAQ/ROI links)
All transceivers mid board, pigtail/octopus
Short traces (6.4/11Gb/s)
Standard FR4
Opto connectors mainly in Z3
Z2 underused
A
B
Z1
Z2
Z3
front panel connectors
C

## Slide 4: Topo prototype / issues
FPGA configuration based on
  Legacy systemACE (10 devices available @ MZ)
  SPI for control FPGA
  Configuration scheme for processors not yet decided
Aggregate RTDP input bandwidth (payload) 286Gb/s per processor @ 6.4Gb/s (573Gb/s per module)
  Consider 10Gb/s option (× 1.5)
  Larger devices on production modules (× 1.4)
What bandwidth do we actually require at phase-0, phase-1 ?
  Will we run CMX plus muon plus eFEX plus jFEX data concurrently into L1Topo for a certain period of time
  For phase-0 we are talking smooth changeover, how about phase-1 ?

## Slide 5: Further issues / concerns
For reason of link integrity and due to unknown data sharing between the FPGAs for specific algorithms, there is no on-board duplication. Have to rely on duplication at source or use data re-transmission on parallel links (latency!) to share data between FPGAs
Is XC7V690T foot-print compatible to XC7V485T (GTH vs. GTX links) ?
Possible line rate gaps of V7/GTH circuits not yet known
Optical power budget depends on tx/rx device pairing : Avago strongly recommend miniPOD on both ends of the fibre, failing that use AFBR-810BEPZ, do not use standard SNAP12 !
What optical power budget do we need ? Fibre length and type, number of connections, quality of connectors, optical splitting, …
What will we require to build a compliant ATCA module ?
What scheme should we use for IP connection ?
Do we actually want ATCA backplane compatibility ?

## Slide 6: Topo prototype
Status
Have started work on detailed design
Bruno looking into
  power distribution
  Cadence symbols
Eduard started looking into PCB level simulation of high-speed links (hyperlynx)