## Slide 1: L1Topo-phase1

## Slide 2: Expanding L1Topo for phase1
Design L1Topo for a life throughout phase 1
Be prepared to take in further data
  Go for maximum line rates (up to 13 Gb/s ?? $$!!)
but
  Not sure what miniPOD maximum rates will be in 2018
  Aggregate bandwidth will also depend on bandwidth limitations on the various data sources
  No foot-print compatible larger processor devices will exist
  In L1Topo2013 we do not plan for backplane connectivity in zone 2 for reason of latency and processor-to-processor bandwidth (dual processor module)

## Slide 3: L1Topo 2013
2 × XC7V690T (A,B)
1 × XC7K325T (C)
14 miniPOD receivers
80 links per FPGA
Possibly up to ~13 Gb/s
Some miniPOD transmitters
All transceivers mid board, pigtail/octopus
Opto connectors mainly in Z3
Little connectivity in zone 2
A
B
Z1
Z2
Z3
front panel connectors
C

## Slide 4: Plans for 2018
Be prepared to manufacture more of the same: in case there is sufficient capability for assembling separate data streams at the sources, several topo processor modules can work in parallel on different algorithms with different input data requirements
Be prepared to build a new topo module that suits the needs of possibly increasing data volume at phase-1
( Mainz determined to work in both directions ! )