## Slide 1: L1Topo Status & Plans
B.Bauß, V.Büscher, W.Ji, S.Krause, U.Schäfer, A.Reiß, E.Simioni, S.Tapprogge, V.Wenzel

## Slide 2
Topo system
Topo processor, post-PDR
Current activities
  Some results from Gold
  Targeting V7
  Zynq
  Service firmware
  Algorithmic firmware
Hardware status
Timeline
Summary

## Slide 3: Topology 2013/14 (RTDP)
Topo Processor
Muons
Legacy electrical links
Cluster Processor
CMX
CTP Core
Jet/Energy Processor
CMX
From PPr / nMCMs
6.4Gb/s fibre bundles
Fibre & 32 electrical LVDS links
160 /
12 /

## Slide 4: Topology Processor
To provide a maximum of flexibility for applying topological trigger criteria:
  Maximise aggregate input bandwidth without compromising on on-board RTDP bandwidth
    Two high-end processors
    820 Gb/s @ 6.4Gb/s (2014 baseline rate)
    Jets, clusters, Muons into single module
    Allow to correlate all trigger object types within full solid angle
Option to run separate algorithms on more than one topology module in parallel
High density 12-channel opto transceivers (miniPODs)
Fibre bundles from L1Calo CMXes and Muons
Both fibre bundle and low latency LVDS into CTPcore
Some critical circuitry on mezzanine, to allow for later mods
Make use of data duplication at source, if required
Well prepared for phase 1:
  accept line rates above 6.4Gb/s from future processors (FEXes, muons)
  Employ zero suppression

## Slide 5: Topo processor details – post PDR
Real-time path:
  14 fibre-optical 12-way inputs (miniPOD)
  Via four 48-way backplane connectors
  4-fold segmented reference clock tree, 3 Xtal clocks each, plus jitter-cleaned LHC bunch clock multiple
  Two processors XC7V690T (prototype XC7V485T)
  Interlinked by 240-way LVDS path
  12-way optical output to CTP
  32-way electrical (LVDS) output to CTP via mezzanine
Full ATCA compliance / respective circuitry on mezzanine
Module control via Kintex and Zynq processors
  Initially via VMEbus bridge
  Eventually via Kintex or Zynq processor (Ethernet / base interface)

## Slide 6: floor plan, so far…
Processor FPGA configuration via SystemACE and through module controller
Module controller configuration via SPI and SD-card
DAQ and ROI interface
  Two SFPs, L1Calo style
  up to 12 opto fibres (miniPOD)
  Hardware to support both L1Calo style ROD interface, and embedded ROD / S-Link interface on these fibres

## Slide 7: … and in 3-d

## Slide 8: Topology Processor Schedule
2010
2011
2012
2013
2014
Technology Demonstrator (BLT)
Functional Demonstrator (GOLD)
Prototype
Installation
GOLD delivery
Production Completed
Production module
Prototype production

## Slide 9: Current activities: module control
Sebastian working on register model (s/w)
Andreas making the fibre-optical VME extension more robust (f/w)
Sascha started work on Zynq processor (FPGA fabric plus ARM processor)
Device chosen for L1Topo (Mars ZX3) not yet available
Currently using Zedboard to get acquainted to the processor and design environment
Got system up with supplied software (Linux) and firmware images
Got networking into usable state, wildly patching initrd image
Major software development effort using cross compiler tool chain (see next slide)

## Slide 10: Module control
Almost done !
Now digging at hardware access
Out of the box there is a GPIO interface implemented in the fabric, allowing for some lights to be flashed from Linux command line
Build L1Topo specific hardware interface (VME-like register model ?) in firmware
Attach the interface to the ARM core and write support software
 need to get used to Xilinx EDK

## Slide 11: Functional Demonstrator : “GOLD”
Fibre input from the backplane (MTP-CPI connectors)
10Gb/s 12-channel industry standard o/e converters on mezzanine
High performance FPGAs (XC6VLX240T) with multiple 6.4Gb/s transceivers
Real-time output via opto links on the front panel

## Slide 12: GOLD TESTS (Virtex-6)
Jitter analysis on cleaned TTC clock (σ = 2.9 ps)
Signal integrity: sampled in several positions along the chain
MGT and o/e converters settings optimization
Bit Error Rate (BER) < 10-16 at 6.4 Gbps / 12 channels
Eye widths above 60 ps (out of 156 ps)
Crosstalk among channels measured in some cases but with negligible effect
Sampled after fan-out chip

## Slide 13: GOLD TESTS (Virtex-6)
Latency measurements done in several configurations at 6.4 Gbs
(16 bit data width and 8/10 bit encoding)
Far End PMA loopback: 34 ns latency
Electrical output: 63 ns latency
Far End PCS loopback: 78 ns latency
Parallel loopback in fabric: 86 ns latency

## Slide 14: GOLD TESTS (Virtex-6)
GOLD is our test-bench for topological algorithms
Logic consumption: a medium size algorithm (sorting algorithm) absorb about 10% of the logic

## Slide 15: GOLD TESTS (Virtex-7)
We are experiencing with Virtex7-VC707 evaluation board using the GOLD as a source
BER cores worked out of the box but there are bugs on the ChipScope Analizer which prevent to run automatic parameters scans
4 channels pulled to 10 Gbs with a not optimized setting and no errors measured in a short data acquisition of half day
Repeating the Latency measurement on Virtex-7

## Slide 16: Service FW
CPLD FW for o/e converters, jitter cleaners, TTCRx
GOLD will used as a source/sink for testing purposes
Feed the VC-707 via SFP with defined data vectors (for V7 latency measurements)
Feed the sorting algorithm programmed in one input GOLD FPGA. Only 12 channels are feed due to HW limitations
In the future the GOLD will feed the TP prototype in a similar way
Improving the communication firmware among the VME extension (BLT module) to the GOLD via SFP fiber

## Slide 17: Summary
L1Topo functional demonstrator (GOLD):
High-speed o/e data paths successfully tested
MGT Parameters tuned at 6.4 Gb/s for large bit-error free windows
Latency measurements taken, activity on-going
L1Topo Prototype:
Design ready, reviewed, schematic capture almost finished
Modifications due to review incorporated
Layout well advanced
Some not yet finalised circuitry to go onto mezzanine module
PDR follow-up in November
Considerable effort going into s/w, f/w, system-level integration
On schedule for installation during shutdown 13/14