## Slide 1: jFEX ROD bandwidth
Baseline jFEX - phi quadrant/eta strip:
6 FPGAs × 80 input links @ 6.4Gb/s  480 links
DAQ data volume probably dominated by inputs
40MHz  100kHz : require 480/400 ROD links per time slice sent.
Scaling up accordingly for phase 2
Assume inputs and DAQ outputs same link type and speed
 1.2-6 MGT links into ROD at phase 1
Allow for some headroom to avoid need for excessively large local buffer
Local buffer needs to be implemented on processor FPGAs !
For the time being assume this input into some external ROD modules