## Slide 1: jFEX
Uli
Intro / overview / issues
Draft, will change !!!!
Some questions flagged

## Slide 2: Intro: L1Calo Phase-1 System / Jets
CPM
JEM
CMX
CMX
Hub
Hub
L1Topo
ROD
ROD
JMM
PPR
From Digital Processing System
CPM
JEM
CMX
CMX
Hub
Hub
L1Topo
ROD
ROD
JMM
PPR
jFEX
CPM
JEM
CMX
CMX
Hub
eFEX
Hub
Opt.
Plant
L1Topo
JMM
New at Phase 1
RTM
RTM
Jets
Phase-1: jet feature extractor jFEX
Finer granularity:
Improve on jet finding (and MET measurement)
Jet size…

## Slide 3: Baseline jFEX input data
  Fibre bundles via patch panel / fibre re-bundling stage
  Granularity .1×.1 (η×φ)
  One electromagnetic, one hadronic tower per η×φ bin
Baseline 6.4 Gb/s line rate, 8b/10b encoding,  128 bit per BC
Up to 16bit energy per tower  8 towers per fibre
LAr data from DPS
Tile … options…
Stick to 6.4 ?

## Slide 4: Sliding Window Algorithms
Phase 0 Phase 1
Baseline ?
Jet elements (towers)
ROIs environment
Increase dynamic range
Improve granularity by factor of four, to 0.1×0.1 (η×φ)
Slightly increase environment (0.9 × 0.9 baseline)
Allow for flexibility in jet definition Fat jets to be calculated from high granularity small jets ?
Optionally increase jet environment
Assume fat tau algorithm resides in same FPGAs

## Slide 5: Data replication
Sliding window algorithm requiring large scale replication of data
Forward duplication only (fan-out), no re-transmission
Baseline: no replication of any source into more than two sinks
Eta-strip / phi quadrant organisation:
Fan-out in phi handled at source only (DPS)
  Transmit “core” and “environment” data
  Duplication at the parallel end (on-FPGA), using additional Multi-Gigabit Transceivers
  Allowing for differently composed streams
  Minimizing latency
Fan-out in eta handled at destination only
  Baseline “far end PMA loopback”
  Looking into details and alternatives
η
ϕ
?

## Slide 6: jFEX module partitioning baseline
Rely on that ?
Enough?
Algorithm requiring environment of 0.9×0.9 around
each tower to be processed  +/- 4 neighbours in eta and phi
Processor modules
  Process strips along eta
  Receive fully duplicated data in phi from DPS
  8 modules covering half of eta, phi quadrant each
  Most cells duplicated in a regular way at both source and sink
  “Irregular” duplication at η=0
  (Current) detector cabling has lower latency around η=0 due to cable path
  Benefit from this latency reserve and use for additional optical fan-out (re-transmission)
η
ϕ
η=0

## Slide 7: jFEX baseline partitioning
Processor modules
Half eta × phi quadrant per module
Total of ~32 × 16 bins × 2 × 2 (upstream duplication, e/h)
~256 incoming fibres @ 6.4Gb/s baseline
22 × 12-way opto modules “MicroPOD” high density receivers
Four 72-way fibre connectors (“MPO/MTP”)
Note: further connectivity required for duplication at η=0: either front (re-transmission) or back (separate active optical fanout station)
Processor FPGAs
Core of up to 1.2×0.8 (η×ϕ), plus environment 0.8×0.8
20 × 16 bins  80 high speed links
6 large FPGAs per module
288 fibres enough ?

## Slide 8: Baseline and options
Phi quadrant baseline driven by need for a rock solid design:
Line rate limited to 6.4 Gb/s only
Avoid extremely dense module
Sufficient η ×ϕ coverage at module level to allow for increase of environment » baseline of 0.9 × 0.9
Orientation along eta might better match Tilecal in phase 2
Backup
In case of problems with η=0 - duplication go for full eta, phi octant scheme
Options
Continue work on higher link speed
Continue work on duplication schemes
Consider slightly larger/more FPGAs
 Increase environment beyond 0.9 × 0.9

## Slide 9: How to fit on a module ?
AdvancedTC A format
6 processors XC7VX690T
4 microPOD sockets each μ
Opto connectors in Zone 3
Fibre bundles from rear F
fan-out via “far end PMA loopback” P
Output to front panel
Readout via backplane
Maximise module payload: small-footprint ATCA power brick, tiny IPMC mini-DIMM
rear
front
P
in
out
μ
7V
F
Z3
ATC250 enough ?

## Slide 10: jFEX system (baseline)
  Need to handle both fine granularity and large jet environment (minimum 0.9×0.9)
  Require high density / high bandwidth to keep input replication factor at acceptable level (~3/4 of all FPGA inputs are duplicates)
  Fit in 8 modules
Single ATCA shelf
Sharing infrastructure with eFEX
  Handling / splitting of fibre bundles
  Some communalities in ROD design
  Hub design
  RTM
η
ϕ
Hub
Hub
L1Topo
ROD
ROD
Optical inputs
Hub
Hub
L1Topo
ROD
ROD
jFEX
Hub
eFEX
Hub
Opt.
Plant
L1Topo
ROD
ROD
RTM
RTM

## Slide 11: Some remarks on baseline
FPGA density reduced wrt previously presented phi ring scheme
Still very dense design, high power dissipation
FPGA count might grow again for larger jet option
Real-time circuitry has absolute precedence over non-real-time components
  Happy to see RODs move off module
  Any TTC solution must be minimum footprint
  Power and ATCA control minimized in floor-plan shown
Baseline design would probably allow for low-latency direct output into L1Topo (48 fibres total)
Output consolidation possible at some latency penalty
jFEX relies on “MicroPOD” high-density optical devices
Aim at higher line rates (currently FPGAs support 13 Gb/s, MicroPOD 14 Gb/s)
Allow for even finer granularity / larger jets / smaller FPGA devices

## Slide 12
Questions and issues are dealt with in following slides. Since I am late, please have a look at them in unformatted shape in the .txt file. They will be added below asap…

## Slide 13: Issues / questions
Many issues that came up recently are common to both FEXes. Concentrate on jFEX specific issues here.
The 6.4 Gb/s baseline is not quite what we want to build
  At module level there is enough environment for large jets
  With FPGAs available on the market that cannot be exploited (excessive on-board duplication)
Is 6.4 Gb/s / 0.9 x 0.9 ok, assuming we will not actually build the baseline but rather increase input rates 2-fold ?