## Slide 1: Response to Comments
Tried to answer all questions that were received by 19:00, Jul. 30
Comments mainly fall into a few categories and can be answered globally:
Typos, improvement on phrasing
  Generally accepted, will be dealt with
Request to add more details (textual description and drawings, including reference to gFEX)
  Generally accepted, will be dealt with
Technical details, in particular latency
  Yes, will be added. Assume no major differences to eFEX figures, except:
    PMA loopback latency is higher (1-1.5 BX estimate)
    Parallel transmission latency figures (to neighbour FPGA) similar (tbc), but nowhere in the system PMA and parallel re-transmission are cascaded
    Transmission to merger same figure
    Regarding algorithms, expect to benefit from improved UltraScale performance

## Slide 2: …
Component availability
  Prototype using engineering silicon, in contact to distributor
Questions about 12.8 Gb/s on inputs and outputs
  12.8 Gb/s operation has been verified in recent past on L1Topo prototype (Virtex-7 GTH, MiniPOD), even though focus has been on 6.4Gb/s operation
  Extensive tests will take place well before jFEX prototype production, on L1Topo spare modules
  Consider L1Topo a demonstrator for jFEX
  jFEX prototype is basically more of the same, re-targeted to UltraScale
  Questions about impact of gFEX on jFEX capabilities
    The overlap between jFEX and gFEX capabilities is intentional and has been judged as important to reduce risk for the phase 1 project. The gFEX endorsement includes a strong recommendation to pursue the full capabilities of the jFEX system at high link speeds