## Slide 1: jFEX and L1Topo module control
L1Topo and jFEX are modular devices
  2/4 instances of processor + opto transceiver on board
  Module control mainly on mezzanines
jFEX prototype in production (almost done)
Decision on L1Topo/Phase-1 asap. Need requirements and clear statement from community
Prototype either
  Current L1Topo/0 or
  Current jFEX (production module will be synthesis of both)
jFEX has all control functionality located on mezzanines
L1Topo/0 has control FPGA on board (eROD,IPbus), but requires some mezzanine rework for Phase-1 anyway.
Aiming at a consistent control scheme for both modules at phase-1
  Module control / IPbus
  FPGA configuration
  Extended environmental monitoring / I2C
  (clock synthesis / jitter reduction)

## Slide 2: L1Topo/jFEX module control history
L1Topo/0
  Standard IPbus
  SystemACE FPGA configuration
  Environmental monitoring / I2C via control FPGA (Kintex)
  No embedded controller
jFEX initially planned for FPGA based control
Started considering change to Zynq based scheme
  Rouven S. has been working on required hardware and software (PetaLinux)
  PicoZed (7030) daughter card on jFEX extension mezzanine
  Required connectivity for control, I2C, configuration, clocking
  Rouven not with our group anymore, lacking Zynq specific effort now
   Use programmable logic resources within Zynq (Artix) only for monitoring, control and configuration.

## Slide 3: Plans
Follow both options (FPGA vs. Embedded controller) at conceptual level for a little while
Live with FPGA-only until further effort on the horizon
Probably base final decision on whether Zynq officially supported in ATLAS DAQ world.
Final decision can be taken at a rather late stage since relatively simple mezzanine. Mainboard not affected. Zynq based scheme might be somewhat more expensive than simple FPGA scheme…
… have to limit effort in control area since busy with real-time stuff…