## Slide 1: Hardware trigger processor demonstrator
L1Global demonstrator presented at June joint meeting
Now going into detailed design phase
Modular design
Base board probably ATCA compliant
Explore ALTERA high performance / high bandwidth FPGAs
  Start with what’s available now: Arria10
  Move on to pin compatible Stratix10 as it comes to the market: 28Gb/s
  Move on to 56Gb/s PAM-4
Finding appropriate optoelectrical transceivers might be challenge
Allow for choice of opto devices by defining daughter module reference pinout
Current favourite: use a couple of Samtec FireFly sockets with defined relative position
 mount two FireFly modules
 mount custom carrier for alternative product (up to 24x)

## Slide 2: demonstrator
Eventually we expect to have a module available with one control FPGA, two high-performance/high bandwidth processors and associated opto fibre connectivity
We are planning to route additional high-speed links onto a mezzanine socket, allowing for connection to an auxiliary processor (eg. GPU via PCIe), should that turn out to be advantageous.
Note: it seems Altera is aiming to get a large variety of heterogeneous multi-chip packages onto the market over the next couple of years. The demonstrator will be built such as to exploit capabilities of further upcoming devices (eg. high memory count devices) if we consider them beneficial for trigger processing purpose.

## Slide 3: demonstrator
Starting as technology demonstrator
  Next generation FPGAs
  Opto transceivers
  PAM-4 encoding
  (GPU optional)
Turn it into functional demonstrator once required functionality becomes clearer
Test bed for firmware development