## Slide 1: DCS on jFEX and L1Topo in Phase-1
Christian/Duc/Uli, Mainz

## Slide 2: Pre-history: Topo in Phase-0
LAPP IPMC available on L1Topo
  Initial firmware work done by Adam
  Readout of all sensors, handle switch, power negotiation
  Not currently in use
Additional data available
  Some environmental data collected by control and processor FPGAs
    Direct FPGA-internal sensing of temperatures and voltages
  Some devices controlled and monitored by I2C (opto devices, clock conditioners,…)
  Sub-set of these data can be sent into DCS via IPbus/OPC server

## Slide 3: L1Topo / jFEX @ Phase-1
New L1Topo based on jFEX mainboard with
Two processors with twelve 12-way optos each
Extension mezzanine with added electrical out to CTP
 jFEX 1st prototype:
Final prototype in production
Available MZ this month
Both L1Topo and jFEX carry LAPP IPMC
Probably move to a more convenient place on L1Topo

## Slide 4: L1Topo module block diagram

## Slide 5: L1Topo components placement
IPMC

## Slide 6: IPMC / Environmental sensors
IPMC design copied from current L1Topo
IPMC not yet functional on jFEX 1st prototype.
Under work. Adam + NN
Coherent scheme between jFEX and new L1Topo
All I2C sensing goes via mezzanine
Route any vital information to the IPMC
Probably small number of data only:
  few voltages
  FPGA temperatures
  FPGA configuration status into DCS ???
Additional expert level interface into IPbus
  Might not be exported to DCS (tbd)
Set of required DCS data and concept of expert level access to extended data set under discussion
… Shelf level monitoring should anyway complement module level monitoring…