## Slide 1: Colour code
Done or almost done
Urgent
Needs attention
Standard priority

## Slide 2: Uli (some duplicates removed)
All FPGAs: FPGA temperature readout currently not working
Processor FPGAs: Muon real-time path is ok. But data are not zeroed on error of neither CRC nor MGT error Calo interface: MGT minimum buffer depth currently set to default Muons: Marek not using MGT buffers at all. If converting MGT interface 16--> 32 bit, either buffered or unbuffered mode possible
Does the mentioned reset pulse register duplication refer to MGT PLL on processors ?
Control FPGA:
PLL lock loss / PLL reset issue i2c/spi taken out of design for suspected timing constraints violations I2C control to TTC dysfunctional or missing. Uli look into JEM code serial number chip. Uli look into JEM code ROD busy, not clear whether associated with clock issue clock monitor LEDs are off, broken ? SystemACE not accessible from Ipbus Marek still using ISE. Synthesis issues/timing. Working on Vivado migration. Large multiplexer on S-link probably not an issue on Vivado
Check TTCdec settings including module ID (address). set by CPLD and resistor network.

## Slide 3: Eduard, some duplicates removed
the correct conversion of XML into slaves  probably done already (Christian)
Stop the menu evolution of L1Topo (L1Calo management)
Implement the FW and test it (Sebastian,Johannes,Me). This is correlated with the one above.
Improve documentation (Marek, Christian, Me) to face unexpected
Prepare SD with design for Physics and plug them in (easy but to be done)
Non essential list of FW task by May:
Fix the ctrlBus_delay_* XML + FW, now it's just horrible
Reduce IPbus speed (or change protocol) to avoid DDR calibration or eye shrinking with increased logic usage
Go back to the IPMC configuration (this can be a task for a student) and
all DCS related FSM panels for L1Topo sub-system
Connect CRC errors flags from muon in readout
Move deserialization for CMX links to 32 bit (ger rid of an extra timing-crossing domain)
Re-write/test CPLD design, the one we run is not the one on the repository
Test / implement readout for special case od delayed muon algorithm
Add BC Reset signal to synchronize the output playback Running-1 pattern for CTP timing calibration

## Slide 4: Sebastian Monitoring
firmware
  algorithm
  histogrammer
  IPbus
Software
  Data: local disk, IS ? …?
  Lumi block IS
Lumi block TTC broadcast (start, stop)
Understand TTC broadcast distribution and broadcast types
Check TTC broadcast connectivity on L1Topo. Uli: initial check:ok.

## Slide 5: Uli
TTC broadcasts
I2C for TTC (needs NN for implementation)
Serial number for TTC (needs NN for implementation)