## Slide 1: L1Topo requirements for Phase-1
  Long established task-force to outline Topological Trigger module requirements in Run-3
  There has been another long hiatus
  But the end is (possibly) in sight
    Many thanks to Ian and Robin for kicking me out of my previous lethargy
  Summary
    All information now gathered (almost)
    Draft document complete (almost)

## Slide 2: Outline of document
Topo input numerology
  All the FEXes
  Also MUCTPI
Trigger requirements
  Topological Triggers
  Non-topological triggers (thresholds, multiplicities)
Strawman Topo Connectivity
  How does it fit into current design?
  How does it fit into upgraded design?
  How do we deal with commissioning period?
    Red as currently missing!

## Slide 3: Outline of Talk
Will only cover the newer material
  Original details are provided in the backup slides
Previously covered:
  FEX output content
  Analysis of simple multiplicity trigger requirements
Covered today:
  Analysis of current topological trigger usage
  Assignment of topological triggers to Topo modules

## Slide 4: ‘Typical’ Topological Menu
TOB types | Approximate number of Algorithms | Physics Case | Location
MU only | 40 | B Physics and S.M. J/psi | MUCTPI
EM only | 8 | J/psi electron | TOPO 2
Jet only | 15* | SUSY, Exotics (MJJ) | TOPO 2
MU + XE | 4* | Exotics (Late) | TOPO 2
MU + EM | 5 | Exotics (LFV) | TOPO 2
MU + Jet | 7* | B-tag | TOPO 2
Jet + XE | 25* | Higgs, SUSY (KF) | TOPO 2
MU + Jet + Tau | 3* | Higgs (Disambiguation) | TOPO 3
EM + Jet + Tau | 3* | Higgs (Disambiguation) | TOPO 3
XE + Jet + Tau | 6* | Higgs (Disambiguation) | TOPO 3
XE + Jet + EM | 15* | J/psi electron (tag/probe) | TOPO 3
EM + Tau | 8 | Exotics (LLP) | TOPO 3
 | * plus more using gFex |  | 

## Slide 5: ‘Simple’ TOPO1 Module
Pure multiplicities
  Replaces CMX
Includes new gFEX outputs
Simple, fast, parallel algorithms
(No Muon inputs or outputs)
Fits into current Topo design
  In terms of i/o

## Slide 6: TOPO2 Module: small topological combinations
Mostly single and double TOB type triggers
Allows gFEX equivalent of JET triggers
No Inter-FPGA communication
Fits into current Topo design
  In terms of i/o

## Slide 7: TOPO3 Module: Multi-TOB combinations
ALL TOB types combined in one place!
Huge input requirement for one FPGA
Better separation possible but…
A Jet+Tau+EM algorithm alone requires 152 links
Clearly doesn’t fit into current Topo design
Question: do we really need two fibres for Jet/EM/Tau TOBs

## Slide 8: TOPO3 in current design
If we can get away with 6/7 TOBs per EM, TAU, JET…
Still a difficult ask for current Topo
Also requires data forwarding, many algorithms will be slow
  Latency problems?

## Slide 9: TOPO3 in upgraded design
TAU fibre is (probably) least sensitive to overflows
But Tau Higgs trigger is one of the big users of Topo, so be careful
Need to study algorithms and compromises
  Most of these triggers using truncated lists anyway?

## Slide 10: Commissioning at Phase-1
Proposal for first week, month (year?):
Old topo(s), maintain Run-2 Topo items
Topo 2+3, develop and test Run-3 Topo items
Topo 3, develop and test simple Run-3 items
Legacy
Simple Items
Legacy
Topo Items
Phase-1
Topo Items
Phase-1
Simple Items
OLD TOPO
TOPO2+3
TOPO1
CTP IN
CTP

## Slide 11: First n days of Run-3
New MUCTPI will be in place
  Timing in possible during LS2 (probably)
  Muon multiplicities + topo algorithms available on day 1 via new route
  Old style Muon to TOPO connectivity gone
    Muon + other TOB triggers not possible in legacy Topo
FEXes and new Topo will be in place (hopefully!)
  But my feeling is much calibration still required with beam
    Individual super-cell timing calibration is basic minimum
    Will need to verify that NO super-cells are triggering early
  Beyond timing, many other ‘calibrations’ are necessary
    Filters, energy, pedestal correction, threshold/isolation tuning
  Until all these are studied with data, new system is unlikely to out-perform legacy trigger
How long will this take?

## Slide 12: Conclusions
Draft document nearing completion
  Current version attached to agenda
Next stage, feedback from task-force
  Via email and a meeting soon…
General conclusions on Topo requirements
  Current Topo design could be stretched to accommodate Phase-1 inputs
    But with inevitable compromises in some algorithms
  An upgraded design with more inputs resolves many of these issues
    Maybe with some smaller compromises, should be studied
    But latency is likely to be critical for some algorithms with either design

## Slide 13: Backup
Talk from previous L1Calo Joint Meeting

## Slide 14: L1Topo for Phase-1 Taskforce Latest News
Updated version of talk given in TDAQ week:
  https://indico.cern.ch/event/538558/contributions/2287652/attachments/1345521/2028470/topo160929.pdf
Warning, much of that talk wrong
  All errors/misunderstandings are/were mine
Taskforce has met three times so far
  Still have work to do

## Slide 15: Reminder: Topo Requirements Task Force - who not to blame
Physics and Trigger Requirements
  Brian Petersen, Martin Zur-Nedden
Topo and Central Interfaces
  Katharina Bierwagen, Thilo Pauly, Uli Shaeffer
FEX Interfaces
  Michael Begel, Weiming Qian, Elena Rocco
Phase-2 and interested parties
  David Sankey, Robin Middleton, Murrough Landon

## Slide 16: Next steps (from 2nd meeting with notes)
I will set up twiki
Also will try to have a first shot at defining i/o for a ‘counting’ Topo module
  Maybe some, but not all simple thresholds can be done here
  Starts to define grouping of information on FEX outputs
Would still like more input on Topo/CTP i/o
Next meeting when I’ve made some progress!
Not done
First attempt will be presented today
I’m still a bit hazy here – next meeting
Held, now I have more to do…

## Slide 17: (Most of) rest of today’s talk
Concentrate on Run-3 commissioning phase
  In many ways the most demanding period before Phase 2
Are the current module specifications and numerology sufficient?
  particularly 3 Topo Processors
What’s the best way to organise the Topo Modules and inputs
  For convenience
  For commissioning purposes
  Do they fully address trigger needs?
Light on details of output, but hopefully good first guess at inputs to Topo

## Slide 18: Commissioning at Phase-1
Is it feasible to start Run-3 with minimal legacy trigger items?
  If so, for how long?
How do we commission new Topo algorithms?
  Note that includes the trivial ones!
  This has proved a difficult issue in Run-2
    And we’ll be commissioning eFEXs, jFEXs, gFEX in parallel
How do we use (possibly) limited CTP inputs to do all of these things simultaneously?
  Do we need a more flexible Level-1 menu?
Or, more ambitiously, run all relevant Run-2
Triggers, while also adding new ones

## Slide 19: Phase-1 Commisioning
CMX x 12
CTP
CTPIN
CTPIN
CTPIN
TOPO x 3 (+?)
electrical links
optical links
optical or
electrical links
EFEX x 24
JFEX x 7
GFEX
Actually legacy Topos will run in parallel with three new Topos
MUCTPI

## Slide 20: The big picture
Proposal for first year:
Old topos, maintain Run-2 Topo items
Topo 1+2, develop and test Run-3 Topo items
Topo 3, develop and test simple Run-3 items
Legacy
Simple Items
Legacy
Topo Items
Phase-1
Topo Items
Phase-1
Simple Items
OLD TOPO
TOPO * 2
TOPO 3
CTP IN
CTP

## Slide 21: Assumptions
Phase-1 Legacy menu is broadly similar to current menu
  Not too unreasonable, if LHC luminosity is really restricted to 1.7x1034 for the next few years
  Details will of course change, and there will be fine tuning
  But in some ways things get simpler if luminosity has no big ramp-ups within one year
Legacy Topo may need streamlining
  Perhaps more controversial
  Probably needed to reduce number of Level-1 items, Topo outputs
  My feeling is that once Topo usage becomes more standard, will focus in on ‘golden’ algorithms
    Rather than having a range, to test out different options
  You can see this sort of development in the stabilisation on ‘preferred’ non-Topo thresholds

## Slide 22: Consequences
We don’t have to think too much about TOPO1 in the first year
  Just consolidate key Topo algorithms into one (?) ‘traditional’ Topo processor
TOPO 1+2 can be used to mirror old Topo items, but with FEX inputs
  The devil is in the details here…
  …but not for this talk
TOPO3 should implement the Phase-1 equivalent of the legacy simple thresholds
  With similar range and multiplicities to the current menu
  Plus some extra ones due to new capabilities (eg gFEX)
  Will concentrate on this for rest of talk
  To do this we have to first understand the current menu

## Slide 23: EM threshold usage
Electron/gamma CMX provides 48 bits
  16 x 3
Multiplicities 4-7 are never used
Only 24 bits of the output are really used
Some thresholds are just alternatives for different luminosities
  Would not really be needed if the menu could be changed more flexibly during year

## Slide 24: Tau threshold usage
Tau CMX provides 48 bits just like EM
Multiplicities 3-7 are never used
Only ~15 bits of the output are really used
The ‘IL’, ‘IT’ are useful labour saving devices for comparing isolation options
  But can easily be done via emulation offline
TAU8 is just for Background
Other low thresholds soon to be superseded by Topo algorithms
NOT USED

## Slide 25: Jet threshold usage
Jet CMX provides 60 bits:
  15 x 2 plus 10 x 3
More extensive usage of most thresholds, multiplicities
Still only ~40 bits of the output are really used
2-3 thresholds either not used, or for very specialised usage
  Probably more naturally performed in a Topo algorithm

## Slide 26: Muon threshold usage
MUCTPI provides 18 bits:
  6 x 3
Also no usage of high multiplicity bit
Only 10 bits of the output are currently used

## Slide 27: Energy Thresholds and Heavy Ions
Total Energy:
  16 thresholds available
  Rarely used in proton-proton
  Probably too few for Heavy Ions
Missing Energy:
  16 thresholds available
  Only 8 are used in current menu
    And half of them are back-up/fall-back thresholds
    No real need for back-up if menu were more flexible
Missing Energy Significance:
  8 thresholds available
  Only 2 used in anger
  Surely the natural territory of Topo and (eventually) gFEX
Note that the needs of Heavy Ions and proton running are quite different
  But we only ever have to support one at a time (hopefully)
  Prefer not to clutter up menu/Topo usage with both sets at the same time

## Slide 28: Summary of Lessons from current non-Topo items
The menu doesn’t come near to occupying all the bits we currently provide
  Though it may very well be occupying all the CTP inputs!
Allowing some breathing space for the Run-3 TOPO 3 outputs, could look something like:
What about the inputs?

## Slide 29: Overall strategy
Each type of FEX provides several copies of the same set of data (TOBs etc)
These copies can be sent to a individual Topo/FPGAs
  But not necessarily ALL outputs to EVERY Topo/FPGA
  Only those that need it for the algorithms they perform
FEX
TOPO
TOPO
TOPO
FEX
Ideally can group algorithms into logical sets requiring subset of TOBs
  To avoid extra latency in FPGA-FPGA link
Easy for simple thresholding algorithms in TOPO3
  May be impossible to avoid in some more complex cases

## Slide 30: eFEX outputs
24 modules, 2 x 16 fibre outputs
  Various options for partitioning of outputs possible
  My current preferred option:
    1 x high priority/threshold EM TOBs
    1 x low+high priority/threshold EM TOBs
    1 x high priority/threshold TAU TOBs
    1 x low+high priority/threshold TAU TOBs
Each link contains up to 7 objects
  eFEX coverage about 2x current CPM
    CPM saturates at 5 TOBs (only occasionally an issue for EM3)
    eFEX saturation at 7+7 TOBs should be easily sufficient
      For Phase-1 anyway, may need re-think for Phase-2
With 4 different link outputs, 8 copies are possible
  More than enough to feed 2 FPGAs in 4 Topos

## Slide 31: jFEX outputs
7 modules, 4 x 12 Fibre outputs
  2 x 12 from Jet/Energy FPGAs (Missing Energy etc)
  2 x 12 from pure Jet FPGAs, separate regions
  Suggest 1 link for Energy TOBs, 2 per jet TOBs
    1st Jet link, all TOBs up to a limit
    2nd Jet link, overflows, if any
Each Jet link contains up to 6 TOBs (??)
  jFEX FPGA region is <2 x current JEM coverage
    JEM saturates at 4 TOBs (currently rare except in HI)
    Saturation at 6+6 should be sufficient in most regions
      Probably also for Forward region
With 3 different link outputs per FPGA, only 4 full copies
  Enough to feed 2 FPGAs in 2 Topos
  Could sacrifice some overflow links for extra energy/priority jet links

## Slide 32: gFEX outputs
1 module, 4 x 12 Fibre outputs
  Similar to jFEX, 1 x 12 for global quantities and 3 x12 for jets, of various types
  Not so easy to describe, as many different jet and global algorithms in parallel
  However, Michael seemed happy with 8 Fibres to each Topo FPGA
    2 from global, 2x3 from local
Less easy to predict link occupancy
  No current system to make an educated guess
  Many different objects
  But hopefully 8 links is generous enough
With 2 different link outputs per FPGA, 6 copies are possible
  Easily sufficient for 3 Topos

## Slide 33: TOPO 3 Connectivity (aka Simple Topo)
Need to work out CTP connectivity
  electrical and/or
  optical
Low latency not such an issue here (probably)
Note, no TAU low threshold/priority inputs
  Only needed by Topo algorithms
Topo 3
Lepton
FPGA
Topo 3
Jet/Energy
FPGA
Fibres
Bits
32
16
(16)
16
48
48
EM
TAU
MU
Energy
j JETs
g JETs
EM low
EM high
TAU high
(MUCTPI)
24
24
24
(8)
j Energy
jJET high
jJET low
g Global
g JET
14
28
28
2
6

## Slide 34: Comments on Simple Topo
Looks feasible in terms of inputs
  But already clear input fibre count is tight per FPGA
  Already at ~80 inputs just for jet inputs
  This looks tighter to me now I’ve understood the jFEX outputs more fully
Note that already reduced maximum required FEX output copies from 6 to 5
  Further reduction possible:
    eg don’t need high priority EM/TAU elsewhere (?)

## Slide 35: Topo Topos Connectivity
Next stage of the process
  Need to understand what inputs needed by each Topo algorithm
  Partition similar algorithms into FPGAs
  Use input link numerology suggested by TOPO 3, see if it is suitable for Topo Topos
Some algorithms require many inputs
  But there mayb be restrictions too in terms of unnecessary combination
    Are high priority/threshold EM objects need at all?
    But jets on their own already take up a large number of links
  Do any algorithms overflow the 80 link input per FPGA?
    I’m hoping not many
    In these cases FPGA-FPGA link is required, plus extra latency
    Or some other alternative…

## Slide 36: A new Topo revision
Already decided to increase Topo output bandwidth
  For Phase-2 compatibility
Could also augment Topo capacity
  Move to Ultrascale FPGA
  120 fibre inputs
  More processing resources
    Current Topo is already very stretched
Obviously a ‘bigger’ Topo is going to be easier to handle
  Less concern about input intricacies
  Probably removes need for FPGA-FPGA added latency
But is it necessary?
  Difficult to be sure, we need to study further

## Slide 37: A brief slide on Phase-2
The Task Force is meant to have at least one eye on Phase-2
  Future re-usability, of Topo, if possible
My Opinion
  Topo (Level-0/1 or whatever) is NOT so important to architectural decisions
  Compared to the rest of ATLAS, it’s not a cost driver
    Complex and costly, yes, but small in number
    Compared to replacing millions of channels of readout, etc
  If you need a new module with a few more links and a bigger FPGA, it’s probably not such a big issue in terms of hardware design
    Once the initial design is well validated
  The real difficulty in Topo is not the hardware, it’s the firmware
    This is probably true independently of the exact number of i/o links etc
  Replacement strategy for ATLAS lifetime
    OPAL had working lifetime of 10 years, also one complete CTP replacement after ~5 years
    We have no experience (yet) of the working lifetime of these complex modules
    Replacing FEXes/Topo/CTP and similar every few years may be a worthwhile exercise anyway

## Slide 38: A brief slide on Phase-2
The Task Force is meant to have at least one eye on Phase-2
  Future re-usability, of Topo, if possible
My Opinion
  Topo (Level-0/1 or whatever) is NOT so important to architectural decisions
  Compared to the rest of ATLAS, it’s not a cost driver
    Complex and costly, yes, but small in number
    Compared to replacing millions of channels of readout, etc
  If you need a new module with a few more links and a bigger FPGA, it’s probably not such a big issue in terms of hardware design
    Once the initial design is well validated
  The real difficulty in Topo is not the hardware, it’s the firmware
    This is probably true independently of the exact number of i/o links etc
  Replacement strategy for ATLAS lifetime
    OPAL had working lifetime of 10 years, also one complete CTP replacement after ~5 years
    We have no experience (yet) of the working lifetime of these complex modules
    Replacing FEXes/Topo/CTP and similar every few years may be a worthwhile exercise anyway
Recent News, Phase-2 Decision:
Phase-2 Topo architecture
likely to be new/different
No need to think too hard
about forward compatibility

## Slide 39: Conclusions
Proposal for Simple Topo connectivity made
  Had one iteration with the task force, leading to some updates
  Need to understand connectivity to CTP
  If reasonable can move onto Topo algorithm connectivity
  Starting to look at current and potential future Topo algorithms
Run 3 setup seems feasible with current module specifications
  But recent understanding of jFEX outputs makes it look tighter than I’d originally thought
  One potential big pitfall: latency
  it might all be a lot easier with new modules containing more links
    Would probably lead to simpler cabling, and less need to distinguish dedicated Topo modules
      SIMPLE IS GOOD
    Maybe some need for fibre spaghetti remains