## Slide 1: IPbus / Flash configurator
(pre) History and some technical details:
Processor configuration (stacked) SPI memories located on eXtension mezzanine
Configuration golden image scheme already tried out on jFEX, ~April, 2018 – using JTAG access
Including verification for bitfiles spanning die boundaries
For a little while already, we had an IPbus slave, capable of reading/writing flash memories on KC705 eval board.
In 2019:
Port that piece of VHDL code (IPbus slave only) to eXtension mezzanine (i.e. target a Zynq device) and include into existent IPbus infrastructure
Write accompanying control software
Results: Writing: ok, reading: ok, standalone verification CRC64/ECMA yet to be completed
However, stuck for a few moments due to occasional packet losses… Hardware ? Network topology ?, …?

## Slide 2: IPbus
Concerns about possible issues with new (actually improved) PHY scheme on the mezzanine 
Quick action earlier this week:
Re-target the complete KC705 IPbus code to the mezzanine
Soak tests
100 Million IPbus operations (UDP) error free as of today
The mezzanine hardware is ok
No issues with the new PHY !!!
… must have been some simple, as yet undiscovered bug in the L1Topo control firmware …