## Slide 1: Slice test – L1Topo
Goal: operate L1Topo real-time inputs with all FEXes and spy on the data
Executive summary: L1Topo operated with input data from all FEXes. Mostly success.
Topo used during test week: new, production module
Few fixes required:
  Update Topo firmware to existent register model
  Load .jed configuration file to CPLD
  Sort out an issue with hub clocking (TTC vs. XTAL)
Individual tests to confirm operation as of previous tests, and uncover remaining issues.
Error counters checked
Apparent clock synch issues confirmed/ruled out via (IBERT) recovered clock monitoring
Data recorded in spy memories

## Slide 2: L1Topo results
gFEX – success
  Clock synchronicity confirmed eventually
  CRC scheme not compatible to the one used on L1Topo, as expected.
  Data received in spy memories
eFEX – partial success
  Data received as sent out by eFEX
  Clock synchronicity difficult to achieve. Possible cause for observed word alignment issues. TBD…
  CRC couldn’t be checked due to alignment issue
  Lack of trailer word in case of zero TOBs unexpected feature (idle pattern instead in trailer word)
Final slice test run with data taken concurrently from all three systems. Data sourced from TREX.
Analysis/interpretation yet to be done
Need to discuss CRC scheme and eFEX idle pattern scheme, and clocking

## Slide 3: Plans
Integrate with algorithms
Extend spy scheme to capture additional data (e.g. algorithm-internal data / sort of XTOBs)
Integrate with readout circuitry
Try to achieve as much integration as possible before next slice test !