## Slide 1: L1Topo and jFEX data reception f/w
Incoming real-time data at 11.2Gbps (jFEX) / 11.2 & 12.8 (L1Topo)
MGT-internal parallel data at per-channel word clock (280/320 MHz)
  Up to 118 clock domains per FPGA  need to synchronize
  Distribution of 118 clock domains over 3 SLRs “challenging”
  Inter-SLR connectivity insufficient for fan-out at 40MHz
Need to synchronize once, and replicate in global 280/320 MHz domain
three Super Logic Regions
MGT
sync
to 40MHz
to 40MHz
to 40MHz
280 / 320 Mbps
MGT
sync
MGT
sync
MGT
sync
MGT
sync
x118

## Slide 2: L1Topo and jFEX data reception f/w
That affects latency:
  Requires synchronizer at MGT word rate
  Need to pipeline SLR crossings
Decided in favour of buffered MGT mode rather than sync in fabric
  Higher latency than phase-alignment alone, but avoid fabric buffer
  Well within previous latency estimates/envelope (Christian)
three Super Logic Regions
MGT
to 40MHz
to 40MHz
to 40MHz
280 / 320 Mbps
MGT
MGT
MGT/buf
MGT/buf
x118