## Slide 1: Status L1Topo
Uli, Julio / Mainz
Hardware
Tests
Readiness for slice test

## Slide 2: Hardware Overview
ATCA board based on jFEX design
2 Virtex UltrascalePlus
Two iterations
Prototype (FDR 01/2019)
Final design presented at PRR 08/2019

## Slide 3: Hardware Overview
U1 Power Mezzanine
U2 Power Mezzanine
Virtex
UltrascalePlus (U2)
Virtex
UltrascalePlus (U1)
Control Mezzanine
Board Voltage Level Mezzanine - 1V8
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Board Voltage Level Mezzanine - 2V5
Board Voltage Level Mezzanine - 3V3
ATCA Power Interface
ATCA board based on jFEX design
  Modular design
2 Virtex UltrascalePlus FPGAs
  XCVU9P-2FLGA2577E
  120 MGTs (GTY) per FPGA
    118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
  Control & Power
  Both compatible with jFEX

## Slide 4: Hardware Overview
ATCA board based on jFEX design
  Modular design
2 Virtex UltrascalePlus FPGAs
  XCVU9P-2FLGA2577E
  120 MGTs (GTY) per FPGA
    118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
  Control & Power
  Both compatible with jFEX
L1Topo 1st production module was delivered in September!!
Main change from prototype: correction of GTY calibration circuit

## Slide 5: Module tests
The prototype module was successfully used in
  Interface tests with all sources (FEXes, MUCTPI) and ROD/hub
  Clock synchronization tests with all sources
  Formatted data / protocol tests with all FEXes
The new production-grade module is being subjected to the full test programme established for the prototype
Standalone tests at home lab
System level tests at the STF

## Slide 6: Mainz Test List
Smoke tests
  Special power sequencing using push-button (step by step), monitoring output current on all voltage rails
  Final power sequencing
JTAG boundary scan
  JTAG chain 1: processor FPGAs
  JTAG chain 2: CPLDs
Connect control mezzanine to L1Topo
Power tests
  Monitoring voltages and currents (including FPGA AUX voltages)
  Ripple measurements
Program all processor FPGAs with a test bit file
  XADC monitoring with automatic shutdown
Short term IBERT tests

## Slide 7: Optical Inputs Validation
Setup
  Data sources:
    2 FTMs: 98+48 outputs
    jFEX: 48 outputs
    L1Topo: 48 Tx
  @12.8 Gbps
  PRBS31
  DFE disabled
Evaluate power consumption
Not a long term test (BER < )
LTP
ALTI
FTM2
Hub
TTC Clock
Source
ATCA FABRIC (BACKPLANE)
FANOUT
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
U1
U2
12 Ch (Optical)
12 Ch (Electrical)
Key
FTM1
L1Topo
FTM1
jFEX
FTM2
FTM1
ATCA FABRIC (BACKPLANE)
All links error free!!

## Slide 8: Summary of Eye Scans
Chart: Open Area of Eye Scan @12.8 for U1
Chart: Open Area of Eye Scan @12.8 for U2
Significant improvement of the eye opening on almost all channels, after correction of the GTY calibration circuit
U1 worse and best eye scan
U2 worse and best eye scan

## Slide 9: Eye Scans - Example
11/10/2019
9
L1Topo Status - L1Calo Joint Meeting
U2
QUAD_227_CH0
U1
QUAD_132_CH1
Prototype
Pre Production
Tx WRONG -> Rx WRONG
Tx OK -> Rx WRONG

## Slide 10: Power Measurement During IBERT Tests
* Extracted from DC/DC converter datasheet
All values within the estimations and in agreement with prototype measurements!!

## Slide 11: Ripple Measurements
Evaluate the ripple with different conditions
Measurements for VCCINT, VCCAUX, MGTAVTT, MGAVCC and MGTVCCAUX on U1 and U2
Oscilloscope setup
  AC coupling with external 50 ohm termination
  Timescale
    2 us/div
    200 us/div
    1 ms/div
  Oscilloscope bandwidth: 1 GHz
MGT voltage rails specification (UG578): “The noise at the power pins should be less than 10 mVpp over the band from 10 kHz to 80 MHz”

## Slide 12: Vout Ripple Results
VCCINT
MGTAVCC
MGTAVTT
MGTVCCAUX
U1
U2
All values within the Xilinx specs!!

## Slide 13: Status summary / slice test readiness
L1Topo has been successfully operated with all interfacing modules - eFEX, jFEX, gFEX, MuCTPI, hub/ROD to various degrees
For all FEX sources formatted data transmission has been successful
Both prototype and 1st production module (few mods) well tested
Hardware ready for slice test
Algo status  see Johannes
Firmware integration of all components almost complete: Christian and Marek still busy on their respective ends
Software : initial tests have been done with standalone software, data streams looked at via spy memory
Significant fraction of IPbus register set implemented
Integration in L1Calo/TDAQ world under way (Holger)