## Slide 1: L1Topo recent work / status / plans
Uli, Julio / Mainz
Hardware
Firmware (infrastructure/control)
Tests

## Slide 2: Hardware Overview
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
Two iterations
Prototype (FDR 01/2019)
Final design presented at PRR 08/2019
  Fix on MGT calibration

## Slide 3: Hardware Overview
U1 Power Mezzanine
U2 Power Mezzanine
Virtex
UltrascalePlus (U2)
Virtex
UltrascalePlus (U1)
Control Mezzanine
Board Voltage Level Mezzanine - 1V8
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Board Voltage Level Mezzanine - 2V5
Board Voltage Level Mezzanine - 3V3
ATCA Power Interface
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
    XCVU9P-2FLGA2577E
    120 MGTs (GTY) per FPGA
        118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
    Control & Power
    Both compatible with jFEX
    CTP interface module (LVDS drivers)

## Slide 4: Hardware Overview
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
    XCVU9P-2FLGA2577E
    120 MGTs (GTY) per FPGA
        118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
    Control & Power
    Both compatible with jFEX
    CTP interface module
L1Topo 1st production module with control mezzanine v3.0
new

## Slide 5: Control Mezzanine v3.0 General Functionalities
Carrier board for the UltraZed-EV
Functionalities
  Hosts the control module of the jFEX/L1Topo mainboard
    Zynq Ultrascale+ ZU7EV-FBV900
  LHC clock cleaning and distribution to processor FPGAs
    Si5345
  Hosts the MasterSPI configuration circuitry for processors
    MT25QU02GCBB8E12-0SIT
  IPBus master
  Hosts the PHY chip (transformer-less scheme)
    VSC8221
  TTC data reception and distribution to processor FPGAs
    HUB1: Using fanout NB7VQ1006M
    HUB2: Reception on one MGT and distribution to processors via IOs
  Communication to mainboard CPLDs (PWR and CTRL_CLK)
  Monitoring and slow control
    MiniPODs (Avago) monitoring viaI2C
    PMBus monitoring
new

## Slide 6: Control Mezzanine v3.0 validation status
Carrier board for the UltraZed-EV
Functionalities
  Hosts the control module of the jFEX/L1Topo mainboard
    Zynq Ultrascale+ ZU7EV-FBV900
  LHC clock cleaning and distribution to processor FPGAs
    Si5345
  Hosts the MasterSPI configuration circuitry for processors
    MT25QU02GCBB8E12-0SIT
  IPBus master
  Hosts the PHY chip (transformer-less scheme)
    VSC8221
  TTC data reception and distribution to processor FPGAs
    HUB1: Using fanout NB7VQ1006M
    HUB2: Reception on one MGT and distribution to processors via IOs
  Communication to mainboard CPLDs (PWR and CTRL_CLK)
  Monitoring and slow control
    MiniPODs (Avago) monitoring viaI2C
    PMBus monitoring
All functionalities have been fully validated on both jFEX and L1Topo!
Ongoing production of final PCBs – total lead time, including assembly: 8 weeks

## Slide 7: L1Topo Module tests / mainboard
The production module was stand-alone tested in the home lab
Power consumption and ripple fully measured and reported
Full Ibert tests of all interfaces at the STF
Ipbus subsystem successfully tested (w. control mezzanine 3.0) at STF
System-level tests at the STF successfully run
  Formatted TOB data successfully received from the FEXes
  Spy data BCReset sync’ed
  L1Accept recorded along with real-time data
  Stable data transmission
  Trailer handling understood, final agreement required (see below)
MUCTPI  L1Topo formatted data transmission tests yet to be done
Recently (double check on prototype  production fixes)
Further link qualification tests: e/o MGT transmitter tests
Keysight DSA91204 – 12 GHz bandwidth
  Differential probe soldered on the miniPOD connector
  Optical transceiver for direct fibre connection
12.8Gb/s PRBS-7 pattern chosen ( reference for jFEX design update)

## Slide 8: Last open issue wrt real-time data transmission: Confirm TX link performance
MiniPOD
Receptacle
5425B Diff Probe Heads
N5426B ZIP Tip
(Soldered on a MiniPOD adapter)
InfiniiMax II Amplifier
Agilent/Keysight DSA91204
MiniPOD
81495A Reference
Receiver
PRIZM to MTP
MTP to LC
LC to ST
Agilent/Keysight DSA91204

## Slide 9: Results – Channel X1Y21
Electrical; TX Setup 3; PRBS7
IBERT; TX Setup 3; PRBS7
Optical; TX Setup 3; PRBS7
Eye opening within miniPOD mask specification
A channel that had hadn’t been well understood in previous tests
Tune the MGT parameters
Make sure we are within MiniPOD specs (reduced swing)

## Slide 10: Conclusions on link data integrity
Very good eye opening for the L1Topo outputs, after properly setting the TX Pre-Emphasis parameters
  Within the miniPOD specification
Validation of the L1Topo Pre-Production module and the GTY calibration circuit
  No significant difference wrt to Prototype
 consider design fully validated

## Slide 11: Firmware status
Algorithms and input mapping has been reported on (Johannes) https://indico.cern.ch/event/884278/contributions/3745259/attachments/2004273/3346895/talk.pdf
Real-time infrastructure (MGTs/SerDes) exists
  Tested with FEXes at STF (protocol tests)
Module control (Ipbus)
  First version exists
    Successfully operated with standalone software throughout STF tests
    Recent improvement on play/spy module (BCR syc)
  Being turned into a common framework L1Topo/jFEX
    Online software for common scheme under way
Along with control mezzanine v3.0 comes a set of f/w
  I2C based monitoring of environmental data
Readout firmware will be ported from jFEX soonish
 Full integration yet to be accomplished: real-time infrastructure / algorithms / control / readout

## Slide 12: A few discussions on input TOB data formats…
Had some initial issues with data formats from FEXes at early STF tests
Mainly sorted out
Some modifications to format specs still possible, not finally signed off
  Discussion on optimal CRC scheme (Jira)
  Request to add BCR bit to trailer of FEX TOBs
  jFEX requested some of the "reserved“ bits in trailer for overflow indication
 Can be sorted out quickly  finalize input firmware soonish

## Slide 13: L1Topo production status
The production PCBs exist
First module has been assembled, successfully been tested and reported on in this presentation
Components available for remaining modules
Expect assembly to take ~ 1 Month after green light from reviewers
Production of a small batch of control mezzanines v.3.1 under way
  No issues with PCB production expected
  Assembly needs to be sorted out (previous batch assembled at CERN !)
CTP interface module exists, ready for tests with CTP and volume production at any time

## Slide 14: Summary / plans
First L1Topo production board successfully tested
Basically ready for production of remaining modules
Firmware components in good shape
  Algorithms see Johannes
  Realtime infrastructure done and tested, minor fixes
  Control firmware being restructured
  Readout under way for jFEX (see Ren-Jie)  port to Topo
Firmware integration time-consuming (multi-die FPGAs)
Ready to install in USA15 in summer