## Slide 1: Status L1Topo
Uli, Julio / Mainz
Hardware
Firmware
Tests

## Slide 2: Hardware Overview
ATCA board (based on jFEX design)
2 Virtex UltrascalePlus
Two iterations
Prototype (FDR 01/2019)
Final design presented at PRR 08/2019

## Slide 3: Hardware Overview
U1 Power Mezzanine
U2 Power Mezzanine
Virtex
UltrascalePlus (U2)
Virtex
UltrascalePlus (U1)
Control Mezzanine
Board Voltage Level Mezzanine - 1V8
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Board Voltage Level Mezzanine - 2V5
Board Voltage Level Mezzanine - 3V3
ATCA Power Interface
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
    XCVU9P-2FLGA2577E
    120 MGTs (GTY) per FPGA
        118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
    Control & Power
    Both compatible with jFEX

## Slide 4: Hardware Overview
ATCA board (based on jFEX design)
  Modular design
2 Virtex UltrascalePlus FPGAs
  XCVU9P-2FLGA2577E
  120 MGTs (GTY) per FPGA
    118 input fibres per processor
    FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
  Control & Power
  Both compatible with jFEX
L1Topo 1st production module with “new” mezzanine

## Slide 5: Control Mezzanine v3.0 - General Functionalities
Carrier board for the UltraZed-EV
Functionalities
  Hosts the control module of the jFEX/L1Topo mainboard
    Zynq Ultrascale+ ZU7EV-FBV900
  LHC clock cleaning and distribution to processor FPGAs
    Si5345
  Hosts the MasterSPI configuration circuitry for processors
    MT25QU02GCBB8E12-0SIT
  IPBus master
  Hosts the PHY chip (transformerless scheme)
    VSC8221
  TTC data reception and distribution to processor FPGAs
    HUB1: Using fanout NB7VQ1006M
    HUB2: Reception on one MGT and distribution to processors via IOs
  Communication to mainboard CPLDs (PWR and CTRL_CLK)
  Monitoring and slow control
    MiniPODs (Avago) monitoring viaI2C
    PMBus monitoring

## Slide 6: Control Mezzanine v3.0 - General Functionalities
Carrier board for the UltraZed-EV
Functionalities
  Hosts the control module of the jFEX/L1Topo mainboard
    Zynq Ultrascale+ ZU7EV-FBV900
  LHC clock cleaning and distribution to processor FPGAs
    Si5345
  Hosts the MasterSPI configuration circuitry for processors
    MT25QU02GCBB8E12-0SIT
  IPBus master
  Hosts the PHY chip (transformerless scheme)
    VSC8221
  TTC data reception and distribution to processor FPGAs
    HUB1: Using fanout NB7VQ1006M
    HUB2: Reception on one MGT and distribution to processors via IOs
  Communication to mainboard CPLDs (PWR and CTRL_CLK)
  Monitoring and slow control
    MiniPODs (Avago) monitoring viaI2C
    PMBus monitoring
All functionalities have been fully validated on both jFEX and L1Topo!!!
Ongoing production of final PCBs – total lead time, including assembly: 8 weeks

## Slide 7: Recent firmware updates
Controller firmware adapted to new mezzanine
    Includes I2C handling for Ipbus readout to OPC server
TTC data handling included
    BCReset and L1Accept forwarded from controller to processors
Infrastructure complete, but expect minor trailer format related changes
Algorithm firmware status reported in different place
Full integration real-time infrastructure / algorithms / control / readout yet to be accomplished

## Slide 8: Module tests
The production module was stand-alone tested in the home lab
Power consumption and ripple fully measured and reported
Full Ibert tests of all interfaces at the STF
Currently under system-level tests at the STF
  Formatted TOB data successfully received from the FEXes
  Spy data now BCReset sync’ed
  L1Accept recorded along with real-time data
  Trailer handling understood, final agreement required (see below)

## Slide 9: A few recent results on link data integrity
While most of the tests were made last year, and results have been reported, we did dig deeper on a few issues recently:
Timing data reception from the backplane (detailed measurements actually made on jFEX, but Topo affected just the same):
FTM shown to lack pre-emphasis from fanout drivers, resulting in bad eyes
Hub-driven lines yield good data eyes
MGT transmitter signals into MiniPODs been measured again
….

## Slide 10: Setup (1)
Eye measurement of Tx on L1Topo (only) with oscilloscope - Agilent/Keysight DSA91204 – 12 GHz bandwidth
Differential probe soldered on the miniPOD connector
Or with optical transceiver for direct fibre connection
Goal: Compare the eye diagrams of two channels
    One with errors (“Bad” Channel X1Y21) and one error free (“Good” Channel X0Y21)
Evaluate impact of Tx pre-emphasis on the eye diagram

## Slide 11: Setup (2)
MiniPOD
Receptacle
5425B Diff Probe Heads
N5426B ZIP Tip
(Soldered on a MiniPOD adapter)
InfiniiMax II Amplifier
Agilent/Keysight DSA91204
MiniPOD
81495A Reference
Receiver
PRIZM to MTP
MTP to LC
LC to ST
Agilent/Keysight DSA91204
Setup 1
Setup 2

## Slide 12: Setup (2)
L1Topo
  Optics and electric signal
@12.8 Gbps
PRBS7
On link X1Y21, errors are observed only with the default setup (IBERT)
Link X0Y21 is error free with all setups (IBERT)
Tests performed on L1Topo Prototype (without GTY calibration circuit)
and on L1Topo Pre-Production (with GTY calibration circuit)
  No significant difference observed between both boards
  All results shown on this presentation are related to L1Topo Pre-Production
Default
TX DIFF Swing: 950 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 0 dB
Setup 1
TX DIFF Swing: 950 mV
TX Pre-Cursor: 4.44 dB
TX Post-Cursor: 4.44 dB
Setup 2
TX DIFF Swing: 870 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 9.12 dB
Setup 3
TX DIFF Swing: 730 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 13 dB
Tx pre-emphasis*
*Details on the GTY datasheet.
This white paper provides a very nice explanation

## Slide 13: Results – “Bad” Channel X1Y21
Electrical; TX Default; PRBS7
IBERT; TX Default; PRBS7
Optical; TX Default; PRBS7
Electrical; TX Setup 3; PRBS7
IBERT; TX Setup 3; PRBS7
Optical; TX Setup 3; PRBS7
Eye opening within miniPOD mask specification
Good eye opening on Vivado Eye Scans with both setups
Eye closed, due to the poor electrical connection

## Slide 14: Results – “Good” Channel X0Y21
Electrical; TX Default; PRBS7
IBERT; TX Default; PRBS7
Electrical; TX Setup 1; PRBS7
IBERT; TX Setup 3; PRBS7
Eye closed, due to the poor electrical connection
Electrical; TX Setup 2; PRBS7
Electrical; TX Setup 3; PRBS7
Good eye opening on Vivado Eye Scans with both setups
Eye opening within miniPOD mask specification

## Slide 15: Conclusions on link data integrity
Very good eye opening for the L1Topo outputs, after properly setting the TX Pre-Emphasis parameters
  Within the miniPOD specification
Validation of the L1Topo Pre-Production module and the GTY calibration circuit
  No significant difference wrt to Prototype

## Slide 16: Ongoing discussions on TOB data formats
Discussion on optimal CRC scheme (Jira)
Request to add BCR bit to trailer of FEX TOBs
jFEX requested some of the "reserved“ bits in trailer for overflow indication

## Slide 17: Plans
Adapt IPbus register map to common L1Topo/jFEX scheme
And finally…
Full integration of all firmware components including readout
Note: timing closure is expected to require quite some effort:
Super logic region crossing might still require quite some massaging !!!

## Slide 18: Backup

## Slide 19: Link data integrity – TTC combined data
Check the backplane signals – TTC combined data (for jFEX, only)
    Differential probe soldered on the zone 2 connector
Evaluate impact of Tx pre-emphasis on the eye diagram
Eye measurement of Tx on L1Topo (only) with oscilloscope - Agilent/Keysight DSA91204 – 12 GHz bandwidth
  Using Hub and FTM (on slot 1) as data sources
  jFEX on slots 4 (short trace) and 11 (long trace)

## Slide 20: Setup – jFEX
Data generated on Hub or FTM, from slot 1
jFEX on slot 4 and 11
@6.4 Gbps
PRBS7
5425B Diff Probe Heads
N5426B ZIP Tip
(Soldered on a MiniPOD adapter)
InfiniiMax II Amplifier
Agilent/Keysight DSA91204
Zone 2
Connector
Default
TX DIFF Swing: 950 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 0 dB
Setup 1
TX DIFF Swing: 950 mV
TX Pre-Cursor: 4.44 dB
TX Post-Cursor: 4.44 dB
Setup 2
TX DIFF Swing: 950 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 9.12 dB
Setup 3
TX DIFF Swing: 950 mV
TX Pre-Cursor: 0 dB
TX Post-Cursor: 13 dB
Tx pre-emphasis*
*Details on the GTY datasheet.
This white paper provides a very nice explanation

## Slide 21: Results – Hub -> jFEX
Hub (1) -> jFEX (4); TX Default; PRBS7
Hub (1) -> jFEX (11); TX Default; PRBS7
Hub (1) -> jFEX (4); TX Setup 1; PRBS7
Hub (1) -> jFEX (11); TX Setup 1; PRBS7
Hub (1) -> jFEX (4); TX Setup 3; PRBS7
Hub (1) -> jFEX (11); TX Setup 3; PRBS7
Hub (1) -> jFEX (4); TX Setup 2; PRBS7
Hub (1) -> jFEX (11); TX Setup 2; PRBS7
IBERT test result:
All links were error free (short term test), even though not all eyes are open with “Default” TX pre-emphasis settings

## Slide 22: Results– FTM -> jFEX
FTM uses an 14 ways fanout to forward the TTC combined data to the node slots
So we can’t see any impact of the TX Pre-Emphasis on the receiver side
    Hub has a direct MGT connection
FTM (1) -> jFEX (4); TX Default; PRBS7
FTM (1) -> jFEX (4); TX Default; PRBS31
FTM (1) -> jFEX (11); TX Default; PRBS31
FTM (1) -> jFEX (11); TX Default; PRBS7
IBERT test result:
All links were error free (short term test), even though not all eyes are open with PRBS7. Errors with PRBS31.

## Slide 23: Conclusions
Very good eye opening for TTC combined data links coming from the Hub, after properly setting the TX Pre-Emphasis parameters
Compared the results for two different node slots – long/short backplane trace
  No significant difference was observed
IBERT test result Hub to jFEX
  All links were error free (short term test), even though not all eyes are open with “Default” TX pre-emphasis settings
IBERT test result FTM to jFEX
  All links were error free (short term test), even though not all eyes are open with PRBS7. Errors with PRBS31.