## Slide 1: Latencies jFEX / L1Topo
2020-09-04

## Slide 2: jFEX - Aug 5 2020

## Slide 3: L1Topo

## Slide 4: Latencies – some thoughts
jFEX latency hasn’t changed for five years
  Continuing to work on latency minimization (sub-ticks)
L1Topo latency (electrical nor optical path) hadn’t changed for more than 7 years
Currently working on L1Topo latency reduction
  optical path / multiplicities
  Processing latency down by one tick in August 5 estimate
  Let’s be optimistic : get processing latency down a further few sub-ticks?
But:
Any correlations between different object types difficult for results on the optical path !
Generally:
Latencies cannot be determined by breaking down to individual contributions inside an FPGA, as they do not add up: t1, t2  t1+t2+X
Total latency is known once it has been measured in fully implemented firmware
Neither infrastructure nor algorithms firmware 100% complete
We are still fighting at the timing closure front
Super logic region concept of large Xilinx FPGAs makes it more difficult than ever before  expect significant SLR crossing latency

## Slide 5: Backup slides

## Slide 6: jFEX, June 2015
edms.cern.ch/file/1256858/1/Working_Draft_Latency_Envelope_4Jun2015.xlsm

## Slide 7: L1Topo, March 2013
edms.cern.ch/file/1256858/1/Working_Draft_Latency_Envelope_05Mar2013.xlsm