## Slide 1: L1Topo status: hardware / tests / production / …
Uli / Mainz

## Slide 2: Hardware Overview
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
Two iterations
Prototype (FDR 01/2019)
Final design presented at PRR 08/2019
  Fix on MGT calibration

## Slide 3: Hardware Overview
U1 Power Mezzanine
U2 Power Mezzanine
Virtex
UltrascalePlus (U2)
Virtex
UltrascalePlus (U1)
Control Mezzanine
Board Voltage Level Mezzanine - 1V8
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Tx
Rx
Rx
Rx
Rx
Rx
Board Voltage Level Mezzanine - 2V5
Board Voltage Level Mezzanine - 3V3
ATCA Power Interface
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
    XCVU9P-2FLGA2577E
    120 MGTs (GTY) per FPGA
        118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
    Control & Power
    Compatible with jFEX
    CTP interface module (LVDS drivers)

## Slide 4: Hardware Overview
ATCA board (based on jFEX design)
    Modular design
2 Virtex UltrascalePlus FPGAs
    XCVU9P-2FLGA2577E
    120 MGTs (GTY) per FPGA
        118 input fibres per processor FPGA
24 MiniPOD: 20 RX + 4 TX
Mezzanines
    Control & Power
    Compatible with jFEX
    CTP interface module (LVDS drivers)
L1Topo 1st production module with control mezzanine v3.1
new

## Slide 5: Control mezzanine v3.1
Carrier board for UltraZed-EV SoM
  Functionality equivalent to v3.0 shown in March TDAQ week, with minor fixes
  3 modules produced
  Currently in use at STF on both jFEX and L1Topo
    During last slice week
Functionalities
  Hosts the control module of the jFEX/L1Topo mainboard
    Zynq Ultrascale+ ZU7EV-FBV900
  LHC clock cleaning and distribution to processor FPGAs
    Si5345
  Hosts the MasterSPI configuration circuitry for processors
    MT25QU02GCBB8E12-0SIT
    IPBus master
      Port selection between backplane or front-panel RJ45 with ETH MUX
  Hosts the PHY chip (transformerless scheme)
    VSC8221
  TTC data reception and distribution to processor FPGAs
    HUB1: Using fanout NB7VQ1006M
    HUB2: Reception on one MGT and distribution to processors via parallel I/Os
  Monitoring and slow control
    MiniPODs (Avago) monitoring via I2C
    PMBus monitoring
new

## Slide 6: Controller test status
Smoke tests, power sequencing
Ripple measurement (MGT)
Power up with UltraZed connected
  Re-check ripple for MGT power rails
JTAG access to Zynq
Booting and configuring from SD card
Ethernet MUX
  Zynq PL (IPBus)
      Backplane / front RJ45
  Zynq PS
I2C access to Si5345 (jitter cleaner)
  Monitor status of inputs and outputs
Reception of TTC clock via backplane with Si5345
Check clock reception at FPGA from Si5345
SPI configuration of processor FPGAs
TTC combined data reception from Hub slot 1
To be done
Monitoring and slow control of Si5345 and mainboards MiniPODs, DC/DC converters
Reception of TTC combined data from Hub slot 2 and distribution to processors via I/Os
Slot dependent IP/MAC
IPBus stress test
 Production
All 3 modules tested:
Done 

## Slide 7: Mainboard test status
One prototype, one production module so far, minor differences
Both generations of modules thoroughly tested in home lab and at the STF (standalone and slice)
Modules successfully tested with formatted input from all FEXes @ STF
Data reception confirmed by (BC sync’ed) spy mem readout
Specific optical attenuation tests done, the last missing one (reviewers’ request) quite recently
All real-time hardware interfaces successfully tested in-depth, including CTP port
Clocking, TTC data, and readout paths successfully tested
Successful operation of IPbus, I2C subsystem, IPMC
Some interfaces tested standalone / IBERT / electrical/optical only
System tests done with non-final firmware

## Slide 8: Further steps
Need to make progress on firmware completion
Due to menu dependency, algorithms will never be “final”, just frozen.
Finalize infrastructure firmware (common code base with jFEX)
Adapt readout firmware (common code)
Integrate infrastructure, readout, frozen algorithms (timing closure)
Then
Repeat slice tests
Confirm latency at system and link level
Some specific tests as requested in the PRR report May 4, 2020
Interface test L1Topo / CTP
Protocol test between MUCTPI / L1Topo
Power consumption and FPGA temperatures under full firmware load
Inter-FPGA parallel LVDS connectivity verification.

## Slide 9: And yet further…
Once tests are finished…
“Volume production”, for a total of 5 modules
PCBs available
Components available
Should take ~6 weeks
Completing the modules in the home lab and testing should happen at less than a week per module
Installation
Installation is what happens before the modules slide in…
Rack situation still unclear (?)
Don’t expect any commuters to go out to CERN any time soon
 Limited effort available at CERN, needs careful planning

## Slide 10: Summary
L1Topo and its mezzanines well and tested
Ready to go into production as soon as:
  A few PRR recommended tests done
  Firmware considerably improved and completed
  Final tests at STF done … including final (*) latency figures
Perhaps some open questions about installation at P1
  (*) final = determined for a snapshot of algorithms integrated with high-speed infrastructure, control, and readout