## Slide 1: fFEX mapping requirements
Phi quadrant mapping
fFEX FPGAs covering a core of pi/2 x full eta range per side
Requiring environment of pi/4 each side shared with neighbour  100 % duplication
Opto fibre bundles at fFEX front panel: 2*12-way ribbon on 24-way MTP (probably)
Do not mix data from any octants on same fibre !!!
Avoid mixing octant data in same 12-way ribbon if possible
Try to also keep octants apart at 24-way MTP level ideally
Expect to cover two quadrants per module.
Limited re-ordering on-module *might* be possible.
Re-ordering between modules will require external unit (FOX)
Symmetry for mapping of +/- eta ? Reflective ? Rotation ? Linear?