## Slide 1: fFEX
Uli / Mainz

## Slide 2: fFEX Status
Current baseline:
  four ATCA modules, Xilinx based
  2 processor FPGAs each : XCVU13P-L2FLGA2577E
  Each FPGA covering a phi quadrant, full eta, one detector end
  25Gb/s links, ~65 per FPGA (depends on fill factor)
capturing requirements for Lar/fFEX interface (somewhat belatedly wrt. schedule)
Mapping requirements discussed earlier this week (backup slide)
Find a suitable Lar/fFEX protocol 

## Slide 3: fFEX input protocol requirements
Sliding window algorithms operate synchronously to LHC bunch clock
synchronize huge number of input links to common clock
Near-fixed & low latency link / protocol required
Keep resource use low
Xilinx MGT block providing synchronous gearbox
Fixed pattern of payload/gaps
Seems to provide near fixed latency at 40.08 MHz bunch clock
  If line rate is chosen appropriately
Any algorithms directly supplied at higher clock multiple might need buffering in terms of sub-ticks
  On fFEX, parts of the synchronizer might need to be replicated in super logic regions (4 per FPGA)
Not sure what would need to be done on Intel FPGAs to achieve compatibility / near fixed latency at source

## Slide 4: conclusion
Looking into suitable fFEX input protocol with
  near-fixed and low latency
  Resource efficient synchronizer required
Prefer common protocol with Global
Though: might possibly need to come up with modifications

## Slide 5: BACKUP

## Slide 6: fFEX mapping requirements
Sliding window algorithms with jet environment .8 in phi (and eta)
Phi quadrant mapping
fFEX FPGAs covering a core of pi/2 x full eta range per detector side
Requiring environment of pi/4 each side shared with neighbour  100 % link duplication upstream
Opto fibre bundles at fFEX front panel: 2*12-way ribbon on 24-way MTP (probably)
Do not mix data from any octants on same fibre !!!
Avoid mixing octant data in same 12-way ribbon if ever possible
Try to also keep octants apart at 24-way MTP level ideally
Expect to cover two quadrants per module.
Limited re-ordering on-module might be possible.
Re-ordering between modules will require external unit (fFOX)
Symmetry for mapping of +/- eta ? Reflective ? Rotation ? Linear ?