## Slide 1: Clock module (and other hardware) - questions rather than answers -
post Palaiseau / pre DESY
nach dem meeting ist vor dem meeting

## Slide 2: Mainz CCC saga, so far…
no requirements known  no specifications written
  „improve reliability, connectivity, jitter, and logic resources“
Current CCC schematics available from the Web
  Reverse-engineer the CCC (A.W.+R.D.)
  Put “all” active components into single FPGA
  Xilinx evaluation board (V6/7) + FMC daughter(s)
Reinhold & Andre working on initial scheme/layout
Open questions :
What active components cannot be moved into FPGA (level translators, comparators…) ?
Protection of FPGA signal lines (2.5V maximum…) ?

## Slide 3: CCC vs. TLU
30.11.11: phone call D. Cussans
Build an „AIDA style TLU“, followed by a simple fan-out, i.e. trigger replicator is distinct from trigger generator
Do the h/w in Mainz
TLU-cum-CCC is FMC daughter
Use reprogrammed DCC for fan-out (not finally agreed)
Understand what asynchronous vs. synchronous trigger means for designers and consumers of clock unit
Non-existent TLU design is non-documented at http://www.ohwr.org/projects/fmc-mtlu/wiki (will improve)
Preferably CERN Cadence libraries to be used for common design(s) – trying to get access to CERN repositories
Hope for some s/w & f/w support from Bristol (how realistic ?)

## Slide 4: Some issues…
Either have to rely on LAPP for providing and programming DCCs (Spartan-3?)
Or MZ build both the clock and the fan-out module with FMC connectors to hook up on Xilinx ML605
Or Mainz provide hard wired fan-out board
  Understand fan-out/busy scheme and AC coupling (bias might be different for asynchronous trigger line, A.W./R.D.)
  Long-term plans (Palaiseau meeting) are assuming crate based rather than table-top installations. Could be 1st candidate. 6U-VME format ?
Fully synchronous processing strongly recommended for FPGA based designs
Synchronous triggering requires additional TDC firmware on all asynchronous inputs (machine interface), plus readout of measured TDC values…
If compatibility to asynchronous triggers were required there would be quite some bias towards a design that is *not* fully FPGA based (discrete replicators at least for the trigger line)

## Slide 5: Before / at DESY meeting
Come to a conclusion what we want and talk to David again
Try to get more information on Kintex-7 board (connectivity!), assuming that we’d rather not buy additional V6 hardware
Finalise (any) one suggested scheme/layout
Will most likely never be built as designed
Get prepared for discussions on synchronous trigger
Prepare slides on clock module development and future LDA ! Who will go / who will present ?
Collect input for
  Number of HDMI fan-out channels
  Jitter
  Form factor
next:
- Reinhold status clock module
- Bruno drawing LDA++
- ???

## Slide 6: And the final solution to it all:
Dear Uli Schaefer,
The Microelectronics Support Centre is pleased to announce that it has finalised an agreement with Calypto for the supply of Catapult via EUROPRACTICE.
Catapult High Level Synthesis reduces design time and verification effort by allowing hardware designers to use pure, untimed C/C++ for ASIC and FPGA design entry. No timing or architectural information is required in the C++ source, but is instead automatically added during the Catapult C synthesis process. This allows designers to quickly evaluate different architectures for given performance/area requirement without modification to the C++ source code.  The only missing link in the tool chain is the
PowerPoint-to-C++ converter !!!!!!!!!!!