## Slide 1: NA62 scintillator test system

## Slide 2: Scintillator test system
Assumption:
Stepper motor controlling position of source/photo tube
Test DAQ taking pulses to verify uniformity
Stepper control linked to DAQ
DAQ VME/Linux/gcc based
Interface to CAMAC
LabView ?
To be discussed:
Protocol stepper <-> DAQ (USB(???), serial, h/w, ?)
Timeline CAMAC interface
LabView drivers ?

## Slide 3: Test system electronics list
Stepper control
Some NIM modules
VME system
CAMAC system
Known to be available
VME:
  Crate
  controller w. h/disk (on loan)
  SLC4 + CERN drivers installed
  a few VME modules (TDC, scaler, ADC?????)
Known to be missing
Power cable for VME crate
CAMAC interface
2nd CAMAC crate for commissioning
2nd VME contoller  need to share R.D. / NA62

## Slide 4: CAMAC controller
6U VME, reduced depth (cost)
  Bus drivers, CPLD
  Module might be physically extended to standard depth, including front panel (K.G.)
CAMAC module populating 2 slots (standard /control)
    Bus drivers, CPLD
    Use modified totem pole drivers rather than open collector
Linked by 50-pin flat cable

## Slide 5: CAMAC controller: some details
VME side (almost) ready for production
  Using ABT bus drivers (48mA), fully compliant with VME specs
  Bus controller is XC95XL programmable chip  needs firmware to be written !
CAMAC side will populate 2 slots. Try and cannibalize old CAMAC controller to get hold of half the stuff
The other half is the programmable one
  Use CPLD again, write firmware !
  Avoid open collector drivers, which are not readily available on the market any more
  Use ABT245 totem pole / tri-state drivers and protect by series resistors
  Provide for Schottky diodes to improve pulldown impedance

## Slide 6: Some remaining issues
CAMAC/VME side lead time 8 working days
CAMAC/CAMAC side ?
Reinhold rather busy with student lab equipment
Protocol stepper <-> DAQ
LabView drivers