## Slide 1: The ATLAS Global Trigger Processor U. Schäfer
High speed data links and processors
Phase-2 Upgrade

## Slide 2: ATLAS Trigger upgrade Phase-2
Re-baptise current Level-1 trigger (Calorimeters & Muons)
 "Level-0" trigger
Add track trigger
Add global level-1 processor

## Slide 3: Level-1 requirements
Currently (ATLAS Runs 1 & 2)
Very low trigger latency (2.5µs) including cabling (!)
Fixed latency, pipelined processor
Dead time-less system
Operating at 40,08 MHz LHC bunch clock or multiples
 Processors based on ASICs and FPGAs only
Separate feature extraction stage for various trigger object types
Post upgrade
Low latency (x10)
Some de-randomizing possible, but still limited latency
Very low dead time is acceptable
Not necessarily tied to LHC bunch clock
 any alternatives to FPGA based scheme ?
Process all trigger objects in one processor (per event) to correlate them

## Slide 4: ATLAS Global Level-1 Processor
Latency: spend on processing, not on routing / buffering !!!!

## Slide 5: Activities -- L1Calo Mainz / PRISMA
Initially: architectural discussions
  First conceptual design under way
  Initially FPGA-based
  A couple of feeder FPGAs
  Powerful processor FPGA
Thorough module level planning / Simulation
  Power
  Thermal (!)
  Signal integrity
  …
Evaluation of high-end processors available on the markets
  Link bandwidth
  Link count
  Processing power
  Xilinx, Altera, … ???... ??? / Eval boards ? GPUs ?
Demonstrator module
  Detailed design from mid 2016
Ask for close collaboration with Detector Lab in several fields of expertise
  PCB simulation
  Generic high-speed link design
  GPU-FPGA communication