## Slide 1: Quite some GOLD...
News from upgrade meeting (US,CM)
GOLD h/w status (BB)
Data transmission firmware and tests for the GOLD (AE,IK,JK)
  Design environment
  GOLD Control path : optical extension of VME --
  RTDP : latency measurements / estimate for CMM++  topo processor

## Slide 2: Upgrade meeting 13.04.2010
http://indico.cern.ch/conferenceDisplay.py?confId=91199

## Slide 3: Upgrade meeting 13.04.2010
Phases A/B/C (topo/full digital/track) in 2015/17/19 ?
Long shutdowns (machine) 15/17/20 ?
Can we complete full L1Calo replacement in 2017 ? (NG)
Phase I topo   phase II processor (NG)
Should we do a CMM++ - only scheme for phase I ? (YE)
Discussion :
Full replacement by 2015 : no , 2017 : possibly
Bricolage scheme of feeding current system from digital frontend disfavoured, in particular since latency advantage (SS) not obvious to others. Need latency assessment !
AFP trigger – what does that mean ? When ?
Is CMM project a h/w or f/w dominated project ?
CMM++ only trigger.
Mainz will do GOLD development line anyway  L1topo  L0Trigger ?
Look into CMM++ local algorithms, AFP ?
Algorithms L0topo ?
Several CMM++s in a custom crate ??????

## Slide 4: GOLD floor plan (approximate)
Z1
Z2
Z3
Opto
L
L
L
L
H
H
H
H
5 * XC6VLX (L,M)
4* XC6VHX (H)
144 multigigabit links in zone 2 (equiv. 22300 bit / BC)
M
890Gb/s
total

## Slide 5: GOLD – current status
Schematics partially done
Routing as shown:
xGb/s links hand routed 
‘Low’ speed links (1Gb/s) to be auto routed