## Slide 1: BLT -- progress report
Backplane test pattern agreed with B’ham (preliminary)
  binary counter 24-bit and 23+1 (odd parity on MSb) + DDR clock
Received SNAP12 Opto transmitter/receiver (Stockholm)
MPO cable ordered  next week
Bruno:
  BLT h/w completed (mechanics, connectors, power-up tests. Some wire mods on configurator daughter card)
Uli:
  Tested and fixed VME access to the BLT FPGA (firmware, VHDL, temporary access requiring manual configuration download into FPGA)
  Create top level description for import of BERT firmware
  Preliminary versions of jet and sum test pattern generators (40Mb/s counters)
To do:
  Complete test pattern generators (further patterns, further clock rates, parity)
  Move VME bus interface into CPLD (non-volatile)
  Get SystemACE configurator up and running (flash card)
external requirements:
  Integration of pattern comparison (BERT) into BLT FPGA
  Software for BLT phase control and error statistics readout