## Slide 1: BLT -- progress report
New backplane data format for more aggressive test vector:
  Send 23 bits of data, along with DDR clock (bit 0) and parity (bit 25)
  One 16-bit binary counter serialised to each data bit
  Have a different run length for each counter (0xFFFF-i)
  Implemented and successfully tested on the jet processor for rates up to 240Mb/s, with serial termination, 2.5V LVCMOS signalling
To do:
  Systematic tests in all JEM slots, possibly at increased rate
  Write document on results
  Schedule tests at CERN/B’ham for combined/CP tests
  Move VME bus interface into CPLD (non-volatile)
  Get SystemACE configurator up and running (flash card)
  Schedule high speed opto link tests (h/w is available now)