## Slide 1: SL1calo – preliminary conceptual design
Current L1Calo http://indico.cern.ch/getFile.py/access?contribId=3&resId=1&materialId=slides&confId=49254#page=8
Phase1 (2014) : keep PPr, JEP, CP as is
Increase backplane transmission rate to CMM, per JEM/CPM port: 25 bit * 40 Mb/s  up to 25 bit * 160 Mb/s = 4 Gb/s
Replace CMM by data concentrator electrical@160Mb/s  optical@3Gb/s ‘official’ concept: low cost FPGAs and discrete serialisers (Stockholm : demonstrator under way)
CMM  quadrant mergers  global merger  CTP
Sam at MSU http://indico.cern.ch/getFile.py/access?contribId=22&resId=1&materialId=slides&confId=49254#page=3
Disadvantage: quadrant processing imposes limitations on algorithms
Try to route maximum data volume into single module:
Aim at ~10 Gb/s with FPGA-internal SerDes: roadmap: 3.2Gb/s now (BLT), 6.5 Gb/s this autumn (Virtex-5) 6.5Gb/s ~ Feb. 2010, 11.2Gb/s end 2010 (Virtex-6)
Algorithms not too challenging (?). I/O bound design. Use SNAP12/MPO
(112[CPM]+32[JEM])*4Gbps / 120Gbps ~ 5 MPO  should fit 1module
 Go quad ! (data rate, not modules)

## Slide 2: ... and the JEMs ?
Current JEMs might well serve their purpose throughout SLHC phase1
...until 2017 ? 2018 ? 2019 ? ...
20th century technology. Will it survive ?
Be prepared for replacement for phase1
(HD: to have replacement PP-daughters ready for phase 1)
Several JEM options. My favourite:
Go optical at the back of the PPr
Per PPM: 5.76 Gb/s JEM data, 11.52 Gb/s CPM data (payload)
1 fibre ~10 Gb/s
 ~80 fibres total to JEP ~ 7*MPO / SNAP12
Could fit two FPGAs on single PCB
However: the system won’t be I/O bound but logic bound (sliding window algorithm)
Small number of modules in single crate. Partitioning ?
Improvements on algorithms ?